## Slide 1
-6
-4
-2
0
2
4
6
Process Analysis Methods
Sigma Quality Management
© Sigma Quality Management, 2025

## Slide 2: Simple Process Analysis

## Slide 3: Low Hanging Fruit
Inefficiency
Description/Exam
ple
Action
Duplication
When we make reservations with most hotel chains, we provide them
with our name, address, etc. When we arrive at the actual hotel, the
probability that we will have to give that same information is usually very
high.
Eliminate unn
ecessary
duplication
Misplaced
Activity
At a famous car manufacturer, the glove box was installed at point “A” on
the line. At point “C,” down the line, the glove box was removed to install
some electrical wiring.
Reorder process steps
Storage
Stored m
aterial, supplies, etc., takes up space and incurs cost.
Examples range from manufacturing
in
-
process inventory
to the “vast”
amount of pens, pencils, and stationery “stored” in office buildings.
Minimize storage,
implement Just
-
in
-
Time
delivery
Transpo
rt
Transportation does not add value to the material or product being
transported (consider also the “transport” of customers through your
processes)
Minimize wasted transports
Motion
Often people do things a certain way because of habit, not because it’
s
the best way to perform a task.
Minimize wasted motion
Inactivity
There’s an old saying, “
A person watching a machine is not working.”
One of our quality friends was curious to know why an automated
production line was shut down when the workers went
on break.
1
Minimize or eliminate.

## Slide 4: The Five “S’s”
“S” | Meaning
Sort | Go through the workplace & sort all materials, equipment, etc. that is not needed to perform the work. Get rid of this stuff!
Shine | Clean the workplace. Remove grease & dirt from equipment, scraps & offal lying around. Hang needed tools in appropriate places – make it easy to obtain tools for the job.
Set-in-Place | Establish responsibilities for maintaining the clean, clutter-free workplace (Joe & Jill clean up the lathe area each shift, Jean & Jack clean up the toolbin)
Standardize | Develop a common method for performing the process (pre-DMAIEC)
Sustain | Ensure the common method is employed each time the process is performed and that improvements are built into the common method

## Slide 5: Was the Process Followed?
START
Is there
a standard that, if
followed, would have
prevented the
event?
Was
the standard
Followed?
NO
YES
NO
YES
Could it have
been followed if
“their life depended
on it”
YES
NO
Either - Create the standard & train, and/or simplify the task or process
Either - Modify the standard & train, and/or simplify the task or process
Was the
individual aware of
the consequences
of their action?
NO
YES
Cultural [~95%] – Organizational “behaviors” require change.
Individual [~5%] – Individual behavior requires adjustment
Inadvertent Error – Point out “bad” effects of the action, if not already obvious
Technique Issue – Discover the required “knack” and train
STANDARD means policies, procedures, training, checklists and other items that are supposed to prescribe the way specific tasks are to be done.
Why Does the Wrong/Inappropriate
Process Exist? Are There Other Cases Like This?
Why Wasn’t a Process in Place? Are There Other Cases Like This?

## Slide 6: Comparative Process Analysis (CPA)
Identify how the process operated when the problem occurred,
Identify how the process operates when no problem occurs, and
Seek out the differences between the two. Adopt the best method of performing the process.
Florida Power & Light – CPA used to evaluate causes of work-site injuries

## Slide 7: Twenty Questions
Where is it done?
What happens?
When is it done?
Why them?
Who does it?
How is it done?
Can we do it some other way?
Can some - body else do it?
Can we do it some other time?
Can we do it some-where else?
Can we do some-thing else?
Better Way
Why do it this way?
Why do it then?
Why do it there?
Why do it?
Reason
Current Method
How?
Who?
When?
Where?
What?

## Slide 8: FMEA

## Slide 9: Managing Reliability
To ensure the reliability of a process, we must manage the process’ failures.

## Slide 10: FMEA Purposes
Checking (and improving) the system's design as it exists on paper.
Identifying those critical components that required extensive testing to determine their reliability.
Planning the system's maintenance program to determine preventive and corrective maintenance actions.
Improving the reliability of existing systems by identifying, ranking, and improving critical components of systems or processes.

## Slide 11: FMEA Example

## Slide 12: 4. List the Failure Mode(s) of the Item
Premature Operation
Failure to Operate at a Prescribed Time/Condition
Intermittent Operation
Failure to Cease Operation at a Prescribed Time/Condition
Loss of Output or Failure during Operation
Degraded Output or Operational Capability
Describes the How, Not the Why

## Slide 13: 6. List the Possible Causes of the Mode
Person
Method
Materials
Machine
Environment
Failure
Mode
Defective Material
Defective Processing
Defective Assembly
Fatigue
Assembly Flaws
Welding Flaws
Construction Flaws
High Temperature
Low Temperature
Humidity
Vi
bration
External Force
Contamination
Chemical Spray
Salt Spray
Mechanical Stress
Temperature Change
Pressure Change
Radiation (UV, Gamma, etc.)
Other Environmental Factor

## Slide 14: 7. Determine Detection Abilities
During Operation
During Construction/Manufacture

## Slide 15: 8. Prioritize Failure Modes/Causes
Risk Priority Number (RPN)
FAILURE PROBABILITY
SCORE
Failure is very unlikely to occur
1
-
2
Failure probability is low based on data from similar components
3
-
4
Possibility exists for failure to occur
5
-
6
Failure probability is high based on data from similar components
7
-
8
Failure is very likely to occur
9
-
10
FAILURE SEVERITY
SCORE
Minor failure that may pass unnoticed by the user
1
-
2
Minor failure that deteriorates item's appearance
3
-
4
Medium failure that causes functional deterioration during operation/use
5
-
6
Major failure that disables operation/use
7
-
8
Critical safety failure resulting in injury or death, or damage to property
9
-
10

## Slide 16: 8. Prioritize Failure Modes/Causes
Risk Priority Number (RPN)
PROBABILITY OF FAILURE DETECTION
SCORE
Possible to detect almost every failure in
-
house prior to construction/assembly
(i.e. at receipt inspect
ion)
1
-
2
Mostly detectable prior to completion of construction/ maintenance. Usually
detected during assembly/fit
-
up
3
-
4
Undetectable until turnover to operations. Most failures detected during startup
or post
-
maintenance testing
5
-
6
Undetectabl
e until use by operations/end
-
user. Most failures detected during
operations/periodic testing
7
-
8
Undetectable until demanded by abnormal condition/ accident, not detectable
during operations/periodic testing.
9
-
10

## Slide 17: 9. Recommend Corrective Actions
Mitigating Severity
Reducing Frequency of Failure
Improving Failure Detection
Poke-Yoke for Human Errors (next slides)

## Slide 18: Poka-Yoke* Approaches and Examples
I. Prevent Errors
A. Eliminate the possibility of the error
  Lawn mower must have safety bar engaged to start engine
  Gas cap tethered to car so it cannot be left behind
B. Delegate decisions
  Cash register calculates change
  One-touch setting for popcorn on a microwave
C. Facilitate tasks
  Program VCR using a program code
  Wires that connect are color coded
II. Mitigate Errors
A. Detect Errors
  Auto-shut off on coffeemakers and irons
  Spell checking in word processor
B. Mitigate Errors
  Radar for collision avoidance
  Automatic correction of spelling errors in a word processor
* Japanese Term for Error Proofing
Notes: This model of ways to error proof is derived from: The principles of foolproofing and their application in manufacturing.
Nakajo, T. and Kume, H. 1985. Reports of Statistical Application Research, Union
of Japanese Scientists and Engineers 32(2): 10-29.

## Slide 19: The Best Poka-Yoke

## Slide 20: The Best Poka-Yoke

## Slide 21: Example of Poka-Yoke type control