## Slide 1
-6
-4
-2
0
2
4
6
Data Collection
Sigma Quality Management
© Sigma Quality Management, 2025

## Slide 2: Data Collection Principles
More is Better
Cost is an Issue
How Fast Does Your Process “Produce” Data
“Tool” Guidance
Sampling

## Slide 3: Data Collection Process
Clarify Data
Collection Goals
·
What questions do you want answered?
·
Link customer requirements to measures.
Develop operational
definitions and
procedures
·
Develop operational definitions
·
New vs. existing data
·
Types of data
·
Plan how to collect and record data
·
Develop sampling procedure
Plan for data
consistency and
stability
·
Validate the measurement system
·
Consider gage R&R
·
Train data collectors
·
Test data collection process
Begin data
collection
·
Collect and analyze data
·
Monitor data
collection activities
·
Provide feedback to data collectors
Continue improving
measurement
consistency
·
Improve on
-
going data collection activities
·
Assign responsibility for measurement system
·
Consider sampling after improvement is seen

## Slide 4: Checksheets
KISS Principle
Use “Check-offs/Check Sheets”
Follow Work “Flow”
Leave Room for Comments
Test the Form
Train the Data Collectors

## Slide 5: Example: Cycle time for loan application processing
Requirement/
Measure
Operational
Definition
Data Source
and Location
Sample
Size
Who Will
Collect the
Data
When Will
Data be Collected
How Will
Data Be Collected
Other Data that
Should be Collected
at the Same Time
Time to
process a
loan
application
Fax date, time,
Decision fax date/time
• Loan
Applications
• Represent- ative
fax center
Tim Smith
Dave Mann
289
During the first week of the month, 10/1/99 to 10/7/99
Randomly selected from September ‘99
• Type of loan
• Amount of loan
• Dealer
• Time of day
• Day of week
How will data be used?
How will data be displayed?
• Identification of the Largest Contributors
• Identifying if Data is Normally Distributed
• Identifying Sigma Level and Variation
• Root Cause Analysis
• Correlation Analysis
• Pareto Chart
• Histogram
• Control Chart
• Scatter Diagrams
• Correlation Analysis

## Slide 6: Sampling - Situations
A hospital “produces” over 30,000 Medical Records a year. The Medical Records department is interested in the accuracy of their coding process.
A manufacturing plant produces 50,000 feet of copper tubing a week. The Quality Control department is interested in the defect rate of the tubing.
A maintenance department “produces” about 1000 work orders a month. The maintenance supervisor is interested in the fraction of work orders that were held up waiting for spare parts.
An engineering department is developing the design of a new screw compressor. They are trying to optimize performance of several key characteristics of the compressor.
An engineer wants to determine if a new type of bearing will have a longer life on large motors.
A pharmacologist wants to determine if a new procedure will reduce the “trough” level of a certain antibiotic in sick newborn babies.

## Slide 7: Simple Random Sampling
1. Create a numbering system for the items to be sampled. Each item must be given a unique number.
2. Select an appropriate sample size. The tool or analysis you are trying to conduct will often guide this decision. For example, to construct a “good” histogram, at least 30 points are needed. (See Section 9 for a more detailed treatment of the “how many” issue).
3. Select random numbers that can range from 1 to the highest number in your numbering system. This can be done from a random number table, or a random number generator, found on many calculators. For example, if the highest number in your system is 980, then you’ll want to select three digit random numbers. Select as many random numbers as you need to meet your sample size of Step 2. If duplicate random numbers appear, or numbers higher than the highest number in your system (i.e. 995), just pick another.
4. Associate the random numbers to the items’ numbers. Pick these items and measure the characteristics of interest to you.

## Slide 8: Random Number Table
16408
81899
14153
53381
79401
18629
81953
05520
91962
04739
73115
35101
47498
87637
99016
57491
16703
23167
49
323
45021
30405
83946
23792
14422
15059
16631
35006
85900
98275
32388
91227
21199
31935
27022
84067
50001
38140
66321
19924
72163
65390
05224
72958
28609
81406
27504
96131
83944
41575
10573

## Slide 9: Interval Sampling
1. Identify the number of items from which a sample will be taken (N).
2. Determine the size of the sample desired (n). (See Unit 9.3 for a more detailed treatment of the “how many” question.).
3. Determine the sampling interval (k) by dividing the number of items by the sample size (k = N/n) and rounding up.
  Note: This procedure applies when the “bunch” already exists. It can be modified slightly for collecting process data by estimating the number of items (N) to be “produced” that day, week or whatever time period is of interest.
4. Randomly select the first item in the sample between 1 and k. Call this item “j.”
5. Pick items j, (j + k), (j + 2k), (j + 3k), etc. until you’ve obtained your sample size. You may have to “cycle back” to the beginning of the item numbers to get the last sample item.