## Slide 1
-6
-4
-2
0
2
4
6
Core Data Displays
Sigma Quality Management
© Sigma Quality Management, 2025

## Slide 2: Variation in Product or Service
Leaving the World of Averages and Entering the World of Dispersion
Coin Toss Exercise:
Flip
1
2
3
4
5
6
7
8
9
10
Result
(H or T)

## Slide 3: Data and Statistics Concepts
Nature of Data – Measurement vs. Count Data
Single Point Measures of Performance
  Central Tendency
  Variability
Central Tendency (e.g., Mean) and Variability (e.g., Standard Deviation) account for most of the information contained in a set of data – Walter Shewhart

## Slide 4: Central Tendency

## Slide 5: Variability

## Slide 6: Line Graph

## Slide 7: Line Graphs
1. Draw a vertical and a horizontal axis on a piece of graph paper.
2. Label the vertical axis with the variable being plotted.
3. Label the horizontal axis with the unit of time or order in which the numbers were collected (i.e. Day 1, 2, 3, . . ., Customer 1, 2, 3, . . . etc.).
4. Determine the scale of the vertical axis. The top of this axis should be about 20 percent larger than the largest data value. The bottom of this axis should be about 20 percent lower than the smallest data value. This let’s you see the best picture of the process’ variability. Label the axis in convenient intervals between these numbers.
5. Plot the data values on the graph number by number, preserving the order in which they occurred.
6. Connect the points on the graph.
7. (Optional) Calculate the mean of the data and draw this as a solid line through the data. This turns the line graph into a run chart - trends and patterns are often easier to see with a run chart.

## Slide 8: Types of Process Variation
Common Cause – “Normal” expected variation in a process
Special (Assignable Causes) – Variation that can be attributed to a specific cause in the process
Inputs
Process
Outputs
Materials
Methods
Equipment
Environment
People

## Slide 9: Run Chart
Defects/Unit
0
2
4
6
8
10
12
14
16
18
1
3
5
7
9
11
13
15
17
19
21
23
25
Unit Number
Defects
Good
Data Collected:
7/29-8/3
A. J. Carr

## Slide 10: Interpretation
Also: Extreme Values

## Slide 11: Decisions in the Face of Variation
Correct Decisions:
Only Common Cause Variation Present
Common and Assignable Cause Variation Present
Errors:
Just Common Cause Variation Present – NOT!
Assignable Cause Variation Present – NOT!

## Slide 12: Variation Decision - Summary
“Our” I
nterpretation
Only Common Causes
Common
Plus
Assignable Causes
Only Common
Causes
Correct Decision
–
If Process is
Not
Capable,
Act to Understand
Process Variables and Improve
Process
Wrong Decision
–
You are
Overreacting to Point
-
to
-
P
oint
Variation!
“True” Situation
Common
Plus
Assignable
Causes
Wrong Decision
–
You Are
Ignoring Possible Opportunities
to Eliminate Assignable Causes
from the Process
Correct Decision
–
Understand
and Eliminate Assignable
Causes from Process

## Slide 13: Bar Chart Examples

## Slide 14: “Bad” Bar Chart
98
97
Survival Rate
-
Open Heart Surgery by Hospital
Hospital
D
H
I
Three “Worst”
Percent

## Slide 15: Pie Chart
Pie Chart of PC Printer Errors - Model PH-6
48
18
12
6
12
32
Low Memory
Paper Jam
Extra
Sheet
Fed
Other
Garbled
Font
Wrong
Font

## Slide 16: Radar Chart
Power
Style
Price
Safety
Handling
Comfort
Economy
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1

## Slide 17: Chart Comparison