## Slide 1
-6
-4
-2
0
2
4
6
Introduction to Control Charts
Sigma Quality Management
© Sigma Quality Management, 2025

## Slide 2: Objectives
Be able to identify the elements of a control chart
Be able to select the “best” control chart for a given indicator
Understand the “theory” of how a control chart works (and why)
Be able to identify and apply a rational subgrouping strategy for a control chart
Be able to apply Control Charts within DMAIEC

## Slide 3: Walter Shewhart
Our Hero!

## Slide 4: CTQs – Managing Customer-Perceived Variability
-
1
.
0
-
0
.
5
0
.
0
0
.
5
1
.
0
1
.
5
Upper & Lower Limits – Customer Derived
Variation – Design & Production Controlled
CTQ
(Critical to Quality)

## Slide 5: Typical Control Chart

## Slide 6: “Simple” Explanation of Control Charts
Problem of Variation – Chance vs. Assignable Causes
Criterion I – General
Given a set of n data to determine whether or not they arise from a constant cause system, do the following:
1. Divide the n data into m rational subgroups (of constant or variable size).
2. Pick the statistics you will use to judge the data. The mean, standard deviation and proportion defective have been shown to be the most useful statistics for this purpose.
3. For each statistic, calculate (using the data) estimates of the average and standard deviation of the statistic, where these estimates satisfy as nearly as possible the following conditions:
  a) If the quality characteristic from which the sample is drawn is controlled with average X-Bar and standard deviation , the estimates used should approach these values as the number of data n becomes very large (i.e. in the statistical limit),
  b) If the quality characteristic is not controlled, the estimates actually used should be those that will be most likely to indicate the presence of trouble (i.e. assignable causes).
4. For each statistic, construct control charts with limits based on the statistic’s estimated average plus/minus three times the statistic’s estimated standard deviation.
5. If a point falls outside the limits of the control chart, take this as evidence of the presence of assignable causes, or lack of control.

## Slide 7: Criteria Comments
Statistics vs. Parameters
  “. . One Unique Distribution . . .”
  Finite Nature of Production Process
  Sequence Order of the Data
Rational Subgroups
Choice of “Three Sigma”
Detecting Assignable Causes
Economy not Probability!

## Slide 8: Subgroup Strategies
Rational Subgroup Defined
Impact of Subgrouping on Control Chart Sensitivity
Within-Group Variation
Between-Group Variation
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
Mean
Standard Deviations
Total Process Variation
Time

## Slide 9: Subgrouping Principles
P | Statement | Observations
1 | Never knowingly subgroup unlike things together | Each subgroup must be logically homogeneous Trim amount – right side, left side (should be separate) Signal – running record that hugs the center line
2 | Minimize the variation within each subgroup | Defines routine background noise Makes chart more sensitive to signals
3 | Maximize the opportunity for variation between the subgroups | If there is a possibility that two things differ, make sure they are in different subgroups Variation will show up in Average Chart (between Subgroups)
4 | Average across noise, not signals | Concentrate the signal and make it easier to detect
5 | Treat the chart in accordance with the data | Subgroup frequency should reflect monitoring and decision frequency appropriate for the process. Single points vs. multiple points
6 | Establish operational definitions for the sampling procedure. | Eliminate subjectivity in measurement process (operator-to-operator) Values obtained under essentially the same conditions

## Slide 10: Assignable Cause - Interpretation
Rule 1:
Rule 2:
Rule 3:

## Slide 11: Assignable Cause - Interpretation
1
3
5
7
9
11
13
15
17
19
1
3
5
7
9
11
13
15
17
19
1
Zone
2
3
1
2
3
1
3
5
7
9
11
13
15
17
19
1
Zone
2
3
1
2
3
Rule 4:
Rule 5:
Rule 6:

## Slide 12: Assignable Cause - Interpretation
Rule 7:
Rule 8:
Rule 9:

## Slide 13: Choosing the “Best” Control Chart
Type of Data – Measurement vs. Count
Sample (or Subgroup) Size
Count Data Issues – Defectives vs. Defects

## Slide 14: Control Chart Selection
CONTROL CHART SELECTION GUIDE
What Data is
to be Charted?
What type of data
is to be charted?
(measurement or
count)
Is a standard applied
to the entire item, or
to the item's elements?
Are the count data
assumptions met?
How is the
data to be
Control Chart
Questions for Count Data
DATA
Measurement
Count
Defectives
Defects
np and p chart
assumptions
met
np and p chart
assumptions
not met
c and u chart
assumptions
met
c and u chart
assumptions
not met
Subgroup size
> 10
Subgroup size
= 1
Subgroup size
Constant
Subgroup size
Varying
Constant
area of
opportunity
Varying
area of
opportunity
X-bar, S
X, mR
np
p
X, mR
c
u
X, mR
X-bar, R
Subgroup size
2 - 10
collected?

## Slide 15: Exercises
For your process, discuss possible subgrouping strategies - present why these could/would be “rational.”
(Optional) If you are already familiar with control charts, compare the basis for control charts presented here with your previous training.

## Slide 16
-6
-4
-2
0
2
4
6
Measurement Control Charts

## Slide 17: Objectives
Be able to construct and interpret (by hand and via Minitab):
  X-bar, R control charts
  X, mR control charts

## Slide 18: X-Bar, R Control Chart
1
3
5
7
9
11
13
15
17
19
Range
Average
UCL - Xbar
CL - Xbar
UCL - R
LCL - Xbar
CL - R
Subgroup

## Slide 19: X-Bar, R Control Chart
Quality
Characteristic
Before
After
Changing Center
Quality
Characteristic
Before
After
Quality
Characteristic
Changing Variability

## Slide 20: Skewed Data
Quality
Characteristic
Mean
Quality
Characteristic
Histogram of Averages,
Samples of Size 15 Each

## Slide 21: X-Bar. R Construction
Collect the Data – Subgroups & Size
R – Chart
  Calculating Ranges
  Calculating Average Range
  Calculating Control Limits

## Slide 22: X-Bar, R Construction
X-Bar Chart
  Calculating Subgroup Averages
  Calculating Grand Average
  Calculating Control Limits
  Drawing the Chart

## Slide 23: Control Chart Constants
Sample
Size (1)
A
2
D
3
(2)
D
4
d
2
2
1.880
-
3.268
1.128
3
1.023
-
2.574
1.693
4
0
.729
-
2.282
2.059
5
0.577
-
2.114
2.326
6
0.483
-
2.004
2.534
7
0.419
0.076
1.924
2.704
8
0.373
0.136
1.864
2.847
9
0.337
0.184
1.816
2.970
10
0.308
0.223
1.777
3.078

## Slide 24: X, mR Control Chart
1
3
5
7
9
11
13
15
17
19
Range
Individuals
UCL - X
CL - X
UCL - R
LCL - X
CL - R
Subgroup

## Slide 25: X, mR Construction
Collect the Data – Subgroups & Size
R – Chart
  Calculating Ranges
  Calculating Average Range
  Calculating Control Limits
  Drawing the Chart

## Slide 26: X, mR Construction
X Chart
  Calculating Average
  Calculating Control Limits
  Drawing the Chart

## Slide 27: Nature of Assignable/Common Causes
Data generated by underlying cause & effect process
Hundreds of Causes, But Which Have Greatest Effect?

## Slide 28: Nature of Assignable/Common Causes
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause

## Slide 29: Nature of Assignable/Common Causes
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause
System Of Causes
Causes Having Affect on a Product Characteristic
Amount of Variation in Product Characteristic Attributable to Each Cause

## Slide 30: DMAIEC & Statistical Process Control
Define
Measure
Analyze
Identify
Execute
Control
Launch The Project
Define Outcomes
Identify Stakeholders
Select Team
Define Initial Process Controls
Implement Process Behavior Charts
Identify Assignable Causes
Identify New Process Controls
Implement New Process Controls
Assess Effectiveness of New Controls

## Slide 31
-6
-4
-2
0
2
4
6
Count-Based Control Charts

## Slide 32: Objectives
Be able to construct and interpret (by hand and Minitab):
  P & np control charts
  C & u control charts

## Slide 33: Count-Based Control Charts
‘Defective” Defined
“Defects” Defined
Binomial Assumptions – np & p Control Charts
Poisson Assumptions – c & u Control Charts (later)

## Slide 34: Assignable Causes – Count-Based Charts
Rule 1:
Rule 2:
Rule 3:
1
3
5
7
9
11
13
15
17
19
Rule 4:

## Slide 35: nP Control Chart
Collecting the Data
Counting the Number of Defectives
Calculating Average No. of Defectives
Calculating UCL, LCL
Drawing the Chart

## Slide 36: nP Control Chart

## Slide 37: p Control Chart
Collecting the Data
Calculating the Fraction Defectives
Calculating Average Fraction Defectives
Calculating UCL, LCL
Drawing the Chart

## Slide 38: p Control Chart

## Slide 39: c & u Control Charts
Poisson Assumptions for c & u Charts

## Slide 40: c Control Chart
Collecting the Data
Counting the Number of Defects
Calculating Average No. of Defects
Calculating UCL, LCL
Drawing the Chart

## Slide 41: c Control Chart
1
3
5
7
9
11
13
15
17
19
# Defects
CL
UCL
LCL

## Slide 42: u Control Chart
Collecting the Data
Counting the Number of Defects & Defect Rate/Subgroup
Calculating Average Rate of Defects
Calculating UCL, LCL
Drawing the Chart

## Slide 43: u Control Chart
1
3
5
7
9
11
13
15
17
19
Defect Rate
CL
Assignable Cause
Subgroup