## Slide 1: Catapult Exercise
Introducing the Catapult

## Slide 2
1. Pin Position
5. # of Rubber Bands
1 or 2
2. Stop Angle
3
3
6. Start Angle
1
Factors used will be limited to:
Factor Levels
1. Pin Position 1, 2, 3, 4
2. Stop Angle 1, 2, 3, 4, 5, 6
3. Cup Height 1, 2
4. Hook Position 4, 5, 6
5. # of rubber bands 1, 2
6. Start Angle 90 to 180 degrees
7. Ball Type Wiffle or Rubber
What Does the Catapult Look Like !
3. Cup Height
1
2
4
2
1
3
4
2
6
5
4. Hook Position
7. Ball Type
Wiffle or Rubber

## Slide 3
How Do You Operate the Catapult !
Each Catapult is needs to be operated by a team of 3-7 people
Team Roles
# of People
3 4 5 6 7
Launcher 1 1 1 1 1
Spotter / Measurer 1 1 1 1 1
Data Entry Clerk 1 1 1 1 1
Factor Setting 1 1 1 1
Quality / Process Checker 1 1 1
Time Keeper 1 1
Ball Returner 1
Lay Aluminum foil
on the floor so the
‘spotter / Measurer’ can
see where the ball lands.
Clamp the Catapult
to the table using
a G-Clamp
Distance (m)

## Slide 4: Catapult Exercises
Exercise 3 - ‘Target Shooting’
(Response Surface Method)

## Slide 5
Exercise 3 - ‘Target Shooting’ (Response Surface Method)
Factors used will be limited to:
Factor (-1) (0) (+1)
Pin Position 1 2 3
Hook Position 2 4 6
Start Angle 140 160 180
Instructions (Part 1)
Create a Box-Behnken design for 3 Factors.
Use the 3 factor/ 3 level combinations
listed below:-
Other Factors will be set at:
Factor Setting
Cup Height 1
Stop Angle 3
# of rubber bands 1
Ball Type Rubber
1) Use the following design:-
Box-Behnken Design
2) Create design in Mintab
3) Set up the catapult and complete 0 repetitions for each trial, record the average for each trial. Replicates designed
4) Enter Data into Minitab
5) Determine the factor level combination to shoot the ball 6.5 meters ?
(Note:- See example on next page for help)
Time Management
You have 30 minutes to set up and complete the experiment
You have 30 minutes to run the analysis and determine the factor level combination.

## Slide 6
Example
Q. What Factor Level Combination do you need to Shoot 4.5 meters ?
Let Y(m) = 5.4 + 1A - 2B + 3.7C Where A & B are discrete factors (-1 & +1)
(Knowledge equation from DOE) C is the start angle and is continuous:-
-1 = 140 degrees
+1 = 180 degrees
-1.682 = 126 degrees
1.682 = 193 degrees
Let A = +1 and Let B = -1:- Y (m) = 5.4 + 1 + 2 + 3.7C
Y (m) = 8.4 + 3.7C
Since we need Y to be 4.5 meters, we solve for Factor C:- 4.5 = 8.4 + 3.7C
4.5 - 8.4 = 3.7C
-3.9 = 3.7C
-3.9/3.7 = C
C = - 1.054
Since level -1 = 140 degrees and level +1 = 180 degrees:-
1 unit = 20 degrees with the center point at 160 degrees
Therefore we can represent the level of -1.054 in degrees = 160 - (1.054 x 20)
= 160 - 21.08
= 138.9 degrees (approximately 139 degrees)
Exercise 3 - ‘Target Shooting’ (Response Surface)
To shoot the ball 4.5 meters, we need C set to 139 degrees, A= +1 & B = -1

## Slide 7
Instructions (Part 3)
From the optimum settings calculated previously shoot the ball 5 times and record the results in
the table below.
Exercise 3 - ‘Target Shooting’ (Response Surface)
Team A
Team B
Team C
Team D
Reading 1
Reading 4
Reading 2
Reading 5
Average
Reading
Reading 3
Which Team was the Closest ?