## Slide 1
-6
-4
-2
0
2
4
6
6.4 Introduction to Control Charts
Sigma Quality Management

## Slide 2: Objectives
Be able to identify the elements of a control chart
Be able to select the “best” control chart for a given indicator
Understand the “theory” of how a control chart works (and why)
Be able to identify and apply a rational subgrouping strategy for a control chart

## Slide 3: Walter Shewhart
Our Hero!
Page 6.4-2

## Slide 4: Typical Control Chart
Page 6.4-3

## Slide 5: Choosing the “Best” Control Chart
Type of Data – Measurement vs. Count
Sample (or Subgroup) Size
Count Data Issues – Defectives vs. Defects
Page 6.4-4

## Slide 6: Control Chart Selection
Page 6.4-6
CONTROL CHART SELECTION GUIDE
What Data is
to be Charted?
What type of data
is to be charted?
(measurement or
count)
Is a standard applied
to the entire item, or
to the item's elements?
Are the count data
assumptions met?
How is the
data to be
Control Chart
Questions for Count Data
DATA
Measurement
Count
Defectives
Defects
np and p chart
assumptions
met
np and p chart
assumptions
not met
c and u chart
assumptions
met
c and u chart
assumptions
not met
Subgroup size
> 10
Subgroup size
= 1
Subgroup size
Constant
Subgroup size
Varying
Constant
area of
opportunity
Varying
area of
opportunity
X-bar, S
X, mR
np
p
X, mR
c
u
X, mR
X-bar, R
Subgroup size
2 - 10
collected?

## Slide 7: Subgroup Strategies
Rational Subgroup Defined
Impact of Subgrouping on Control Chart Sensitivity
Within-Group Variation
Between-Group Variation
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
Mean
Standard Deviations
Total Process Variation
Time
Page 6.4-8

## Slide 8: “Simple” Explanation of Control Charts
Problem of Variation – Chance vs. Assignable Causes
Criterion I – General
Given a set of n data to determine whether or not they arise from a constant cause system, do the following:
1. Divide the n data into m rational subgroups (of constant or variable size).
2. Pick the statistics you will use to judge the data. The mean, standard deviation and proportion defective have been shown to be the most useful statistics for this purpose.
3. For each statistic, calculate (using the data) estimates of the average and standard deviation of the statistic, where these estimates satisfy as nearly as possible the following conditions:
  a) If the quality characteristic from which the sample is drawn is controlled with average X-Bar and standard deviation , the estimates used should approach these values as the number of data n becomes very large (i.e. in the statistical limit),
  b) If the quality characteristic is not controlled, the estimates actually used should be those that will be most likely to indicate the presence of trouble (i.e. assignable causes).
4. For each statistic, construct control charts with limits based on the statistic’s estimated average plus/minus three times the statistic’s estimated standard deviation.
5. If a point falls outside the limits of the control chart, take this as evidence of the presence of assignable causes, or lack of control.
Page 6.4-10

## Slide 9: Criteria Comments
Statistics vs. Parameters
  “. . One Unique Distribution . . .”
  Finite Nature of Production Process
  Sequence Order of the Data
Rational Subgroups
Choice of “Three Sigma”
Detecting Assignable Causes
Economy not Probability!
Page 6.4 11-13

## Slide 10: Exercises
For your process, discuss possible subgrouping strategies - present why these could/would be “rational.”
(Optional) If you are already familiar with control charts, compare the basis for control charts presented here with your previous training.