## Slide 1
-6
-4
-2
0
2
4
6
6.7 Measurement System Analysis
Sigma Quality Management

## Slide 2: Objectives
Understand how a measurement system “adds” variation to the observed process event
Be able to identify the sources of error contributed by a measurement system
Be able to plan, conduct and analyze a Gage R&R study using Minitab

## Slide 3: Measurement System Components
The instrument or measuring device
The human operator of the device
The product (or process event) itself
The measurement process (including environment)
Page 6.7-2
Event
Instrument
Observer

## Slide 4: Errors in a Measurement System
Bias
Variation
  Repeatability
  Reproducibility
Stability
Linearity
Page 6.7 2-3

## Slide 5: Resolution
Page 6.7-5

## Slide 6: Other Properties
Statistical Stability
Variability – Related to Process and/or Tolerances
Page 6.7-6

## Slide 7: Measurement System Studies
Study Type
Reference Page(s)
Discrimination
19
Stability
21, 41
Bias
26, 42
R
epeatability
27, 43
Reproducibility
30, 43
Part
-
to
-
Part Variation
31
Linearity
35, 76
Attribute Gauge Study
81
AIAG Measurement Systems Analysis Reference Manual
Page 6.7-8

## Slide 8: Gage R&R Study
Identify the gage (instrument) to be assessed.
Identify the operators who will measure the parts (Joe, Sally, Harry)
Obtain parts from the production process (try to get parts whose characteristic (i.e. dimension) spans the width of the process variation).
Check – To make sure you have enough data for the analysis, the product of #operators (O) times the #parts (P) is greater than 15 (O x P > 15).
Obtain the specification limits for the process characteristic.
Have the operators measure the parts. Arrange the measurement order so that they don’t know which part is being measured (i.e. randomize the order of the measurements). Ensure that each operator measures each part at least twice. If it is not practical to meet the O x P criteria above, you will need to increase the number of times the operators measure the parts.
Conduct ANOVA (Unit 10.3) to understand the total variation, and the components (parts, repeatability, reproducibility, error). Most quality statistical packages (Minitab) have special routines to provide you with both graphical analysis of the study and analytic (ANOVA, variance, standard deviation components).
Analyze the results and determine your course of action (measurement system OK, needs improvement).
Page 6.7 8-9

## Slide 9: Gage R&R Study Data
Part
Operator
Response
Part
Operator
Response
Part
Operator
Response
1
Henry
0.65
1
Henry
0.60
2
Henry
1.00
2
Henry
1.00
3
Henry
0.85
3
Henry
0.80
4
Henry
0.85
4
Henry
0.95
5
Henry
0.55
5
Henry
0.45
6
Henry
1.00
6
Henry
1.00
7
Henry
0.95
7
Henry
0.95
8
Henry
0.85
8
Henry
0.8
0
9
Henry
1.00
9
Henry
1.00
10
Henry
0.60
10
Henry
0.70
1
Beth
0.55
1
Beth
0.55
2
Beth
1.05
2
Beth
0.95
3
Beth
0.80
3
Beth
0.75
4
Beth
0.80
4
Beth
0.75
5
Beth
0.40
5
Beth
0.40
6
Beth
1.00
6
Beth
1.05
7
Beth
0.95
7
Beth
0.90
8
Beth
0.75
8
Beth
0.70
9
Beth
1.00
9
Beth
0.95
10
Beth
0.55
10
Beth
0.50
1
Marilyn
0.50
1
Marilyn
0.55
2
Marilyn
1.05
2
Marilyn
1.00
3
Marilyn
0.80
3
Marilyn
0.80
4
Marilyn
0.80
4
Marilyn
0.80
5
Marilyn
0.45
5
Marilyn
0.50
6
Marilyn
1.00
6
Marilyn
1.0
5
7
Marilyn
0.95
7
Marilyn
0.95
8
Marilyn
0.80
8
Marilyn
0.80
9
Marilyn
1.05
9
Marilyn
1.05
10
Marilyn
0.85
10
Marilyn
0.80
Page 6.7-9

## Slide 10: Gage R&R Results - Minitab Software Analysis
Gage name: ExactoMeas - Dimensions
Date of study: 2/14/03
Reported by: HDUNN
Tolerance:
Misc:
Two-Way ANOVA Table With Interaction
Source DF SS MS F P
Part 9 2.05871 0.228745 39.7178 0.00000
Operator 2 0.04800 0.024000 4.1672 0.03256
Operator*Part 18 0.10367 0.005759 4.4588 0.00016
Repeatability 30 0.03875 0.001292
Total 59 2.24912
Gage R&R
%Contribution
Source VarComp (of VarComp)
Total Gage R&R 0.004437 10.67
Repeatability 0.001292 3.10
Reproducibility 0.003146 7.56
Operator 0.000912 2.19
Operator*Part 0.002234 5.37
Part-To-Part 0.037164 89.33
Total Variation 0.041602 100.00
StdDev Study Var %Study Var %Tolerance
Source (SD) (5.15*SD) (%SV) (SV/Toler)
Total Gage R&R 0.066615 0.34306 32.66 34.31
Repeatability 0.035940 0.18509 17.62 18.51
Reproducibility 0.056088 0.28885 27.50 28.89
Operator 0.030200 0.15553 14.81 15.55
Operator*Part 0.047263 0.24340 23.17 24.34
Part-To-Part 0.192781 0.99282 94.52 99.28
Total Variation 0.203965 1.05042 100.00 105.04
Number of Distinct Categories = 4
Description of Gage, Study “Demographics”
Analysis of Variance (ANOVA)
This analysis shows that the parts are a significant source of variation (good), there is a difference by operator and there is an interaction between the operator factor and the parts factor
Contribution to Variance
Shows breakdown of variance into components – here, the measurement system represents about 11% of the total variance. Of this, 7% is due to reproducibility issues, 3% to repeatability (within the operator).
Contribution to Standard Deviation, Tolerance
Shows breakdown of standard deviation and percentages relative to the total variation and to the tolerance width. Used to calculate Gage R&R, %P/T
Assesses the resolution of the system – 4 or higher is “adequate”
Page 6.7-10

## Slide 11: Minitab Graphical Summary
Page 6.7-11

## Slide 12: Diagnostics
High Bias
Inadequate Repeatability
Inadequate Reproducibility
Lack of Stability
Poor Linearity
Part-to-Part Variation
Acceptable vs. Marginal Measurement System
Page 6.7 12-13

## Slide 13: Measurement vs. Process Variation
Total Observed Variation (TV)
Inherent Process Variation (PV)
Measurement Variation (R&R)
Page 6.7-14

## Slide 14: Measurement System Analysis: % R&R
% Repeatability & Reproducibility - Addresses what percent of the Total Variation is taken up by Measurement Error
Process Variation
measurement system variation
%R&R = 20%
%R&R = 75%
% R&R = 100%
Look for
% R&R < 30 %
Where SMS = measurement standard deviation Where STotal = total standard dev. (incl. process)

## Slide 15: Interpreting Gage %R&R
General guideline for interpreting Gage R&R results— depends on the Process!
Unacceptable
Desired
Acceptable
Borderline
0%
10%
20%
30%
100%
Measurement system is capable of detecting process improvements
and detecting out-of-trends quickly

## Slide 16: Measurement System Analysis: %P/T
Product Tolerance
Lower Spec
Upper Spec
P/T = 20%
P/T = 100%
P/T = 150%
Desired: 10 %
Borderline: 30 %
Precision to Tolerance Ratio - Addresses what percent of the Tolerance is taken up by the Measurement Error
MEASUREMENT SYSTEM
measurement system variation

## Slide 17: Interpreting P/T
General guideline for interpreting Precision to Tolerance results.
Unacceptable
Desired
Acceptable
Borderline
0%
10%
20%
30%
100%
Measurement system is suitable for
product acceptance testing

## Slide 18: Exercises
Gage R&R – Setup, run and analyze a Gage R&R study using the measuring system and parts provided by your instructor.
Your CTQs – Apply Measurement System principles to your data collection (how will you minimize bias, repeatability, reproducibility, linearity)