## Slide 1
-6
-4
-2
0
2
4
6
14.2 Conceptual Design
Sigma Quality Management

## Slide 2: Objectives
Be able to identify a “Static” vs. “Dynamic” design opportunity
Be able to generate design concepts for a new product or service
Be able to parametrically evaluate different existing products or services
Be able to select the “Best” design concept through the Pugh convergence method

## Slide 3: Pugh’s Static vs. Dynamic Designs
Some Designs are “Static” – Basic Concept (e.g., Solution) is Well Established, CTQs Can be Defined With Knowledge of the Concept
Some Designs are “Dynamic” – Choice of Concepts is Open to Team, CTQs Should Then be Solution-Independent
Basic Car Concept has Included: Engine, Transmission, 4 Wheels, Passenger Compartment for the Last 100 Years!
Lighting Concepts Could Include: Incandescent, Fluorescent, LED, Mercury-Vapor, Others
Page 14.2-3

## Slide 4: CTQ Definition Approach
Methods: Customer Needs Research, Quality Function Deployment (QFD)
Dynamic Design:
Methods: Conjoint Analysis, Kano Analysis, Rapid Application Development (RAD)
Static Design:
Page 14.2-4
Market Research/ Consumer Needs
Conceptual
Design
Requirements Definition
Market Research/ Consumer Needs
Requirements Definition
Conceptual
Design

## Slide 5: Concept Development
Analogy (See Forced Analogy)
Attribute Listing (See Attribute Listing)
Inversion (See Problem Reversal)
Page 14.2-6

## Slide 6: “Systematic” Invention - TRIZ
TRIZ - The Theory of Inventive Problem Solving
Genrich Altshuller
- Our Hero!
Page 14.2-7

## Slide 7: Why TRIZ?
Demands on engineers and product developers are overwhelming.
Competitive & customer pressures for innovation & improved value
Compressed development time
Difficult warranty problems/campaigns
Life cycles becoming shorter
Corporate downsizing (Head count reduction)
Products are becoming more complex
What was considered superior yesterday is only satisfactory today, and will be inadequate tomorrow.
Customers have more choices, have become more educated, and more particular.
We need to significantly improve the engineers ability to quickly solve difficult and seemingly impossible engineering problems which often lead to next generation “innovative” products.
Page 14.2-7

## Slide 8: Introduction to TRIZ
Developed by Genrikh Altshuller:
  A brilliant inventor and Navy patent investigator
  Made his first invention at the age of 14 on an underwater breathing apparatus
  Degree in Mechanical Engineering
Altshuller was tasked by the Russian government to study worldwide patents to look for strategic technologies the Soviet Union should know about.
He learned that in a macro sense, Technical Systems exhibited a predictable, and repeatable product evolution.
Page 14.2-7

## Slide 9: Altshuller’s Ideas & “Product”
Some of the same principles were used over and over again by totally different industries, often separated by many years, to solve similar problems.
Knowledge about inventions may be organized, and generalized in order for other inventors or problem solvers to have easy access to the information.
Created extensive “knowledge-base” which includes numerous physical, chemical, and geometric effects along with many engineering principles, phenomena, and patterns of evolution.
Page 14.2-7

## Slide 10: So What is TRIZ?
A method to dramatically increase the engineer's knowledge, creativity, and problem solving skills by sharing the knowledge and experiences of thousands of “silent” former inventors to aid in problem solving.
A method of “Systematic Innovation!”
A method to consciously evolve technological systems and/or to solve engineering problems.
A tool for eliminating engineering conflicts, not compromising by making trade-offs.
Page 14.2-7

## Slide 11: Compiling Innovation
TRIZ provides access to the most effective solutions to technical problems independent of industry.
The reason TRIZ works is that it has been shown that 90% of problems engineers face have been solved somewhere before.
Development is much more efficient if we can utilize this information – move from trial and error to systematic invention!
TRIZ’s main focus is surfacing, understanding, intensifying, and eliminating conflicts.
Important Note: The Power to Apply TRIZ is Directly Proportional to Your Knowledge of the Sciences!
Page 14.2-7

## Slide 12: Basic TRIZ Problem Solution Path
1. ID Current
Problem
5. Analogic
Thinking
Your
Solution
2. Translate to
Standard Problem
4. Investigate
Standard Solution
3. Use TRIZ
Knowledge-base
Your
Solution
Page 14.2-7
Notes: The problem is formatted and modeled.
The model is translated into a standard problem.
Through the TRIZ knowledge-base, the standard problem has several standard solutions.
The standard solutions are examined by Analogic analysis (reverse abstractions); a conceptual solution is generated.

## Slide 13: TRIZ Key Elements
Patent Data Base - Access to the Knowledge Base of the World
Harnessing the Product Life Cycle “S-Curve”
Structuring and Solving the “Right” Problem
ARIZ – The Innovation Algorithm
Design Conflict Resolution
Page 14.2-7

## Slide 14: Contradictions in Design
Difficult engineering conflicts too often resolved by making trade-offs. (This is easy, but something or somebody always loses!)
Five Common Strategies to Deal with Conflicts:
  1. Turn a Strong Conflict into a Strong “Bonus”
  2. Turn a Strong Conflict into a “Non-Issue”
  3. Turn a Strong Conflict to a “Weak Conflict”
  4. Trade Off or Compromise
  5. Ignore and “Hope it goes away”
(Note: Strategies 1, 2, & 3 will need design changes or innovations.)
E
A
S
I
E
R
H
A
R
D
E
R
Page 14.2-7

## Slide 15: Contradictions
Engineers deal with the following types of contradictions:
  Administrative - (AC)
  Technical - (TC)
  Physical - (PC)
TRIZ provides the foundation for inventive “contradiction-busting” solutions.
Page 14.2-7

## Slide 16: Administrative Contradiction: (AC)
The initial definition of the situation with the imbedded contradictions facing the solution seeker.
  A “management” description that defines a desirable but elusive condition.
  Example: We need to accomplish ______ but haven’t a clue how to do it.
Page 14.2-7

## Slide 17: Technical Contradiction: (TC)
When one or more elements or parameters of a system are in conflict.
As one parameter is improved, the other is degraded.
Most systems have numerous, imbedded technical contradictions.
  Example: Power vs. Fuel Consumption
  Weight vs. Strength
  Close Shave vs. No skin cuts
  Others?
??
Page 14.2-7

## Slide 18: Physical Contradiction: (PC)
A CTQ that should be in two self-opposing or mutually exclusive states:
The question to ask to determine the PC:
  What parameter must be in two opposite states in order to resolve the Technical Contradiction?
Within TCs, there is often a PC.
  Solving the PC provides more elegant solutions.
Rigid & Flexible
Sharp & Dull
Wide & Narrow
Hard & Soft
Long & Short
There & Not there
Thick & Thin
Hot & Cold
Page 14.2-7

## Slide 19: Some Inventive Principles
Page 14.2-9

## Slide 20: Parametric Analysis
Gather as much information as possible on your own and your competitions’ products/services (including products/services from outside your industry).
Using a free-form approach, cross-plot the data (one parameter against another) and look for patterns and relationships between parameters.
Start with the logical relationships (e.g. car weight and fuel consumption, air conditioner cooling capacity and energy consumption), but be willing to explore other, unusual relationships – this is generally where the “Ah-ha’s” will be found.
Make sure that you are comparing apples to apples in the comparisons.
Look for patterns in the cross-plots and look for exceptions to the patterns. Regression analysis (including confidence bounds on the plots) can help identify both patterns and outliers/exceptions.
Draw conclusions from the plots – Ask “Why” for the exceptions noted.
Page 14.2-18

## Slide 21: Parametric Analysis
Manufacturing Cost of A/C Unit
Warranty Cost of A/C Unit
A
B
Page 14.2-19

## Slide 22: Pugh Concept Selection Process
Page 14.2-23
Criteria
Rating
A
-
Current
Classroom
(Datum)
B
-
CD
-
ROM
Only
C
–
CD
-
ROM
Plus Classroo
m
D
-
Self
-
Paced
Training Manual
Quality (Learning Effectiveness)
D
Builds Knowledge in Subject
5
A
S
S
-
Builds Skill in Subject
5
T
-
S
S
Allows Learning Application to Own Project (Immediate)
3
U
S
+
-
Compatible with Different Learning Styles
(e.g. via Multiple Media)
3
M
S
S
-
Stimulates Learner Interest and Engagement:
· Effective Presentation (e.g. Live, Text, Graphics, Video)
3
S
S
-
· Ability to Interact during Learning
3
-
S
-
· Ability to Practice Knowledge and Skills
4
-
S
-
· Ability to Ask Questions/Get Answers during Learning
4
-
S
-
· Availability of Expert Advice
3
-
S
-
· Delivery Matches Participant Expertise
4
S
S
S
Ability to Simulate Group Work
2
-
S
-
Evaluation of Knowledge and Skills
3
S
S
S
Learner Se
lf
-
Evaluation
4
S
S
+
Consistent Quality of Instruction
4
+
+
+
Use as Reference Tool Throughout Project
4
+
+
+
Delivery (Access, Time to Obtain K&S)
Learning Efficiency (Time to Learn)
5
+
-
+
Search Capability
4
+
+
S
Self
-
Paced Learnin
g Opportunity
4
+
+
+
Hardware/Software Platform Compatibility
4
S
S
+
Cost of Service
Course Costs
5
+
S
+
Travel and Living
4
+
S
+
Time Away from Work
3
+
S
+
Sum of Positives
0
8
5
9
Sum of Negatives
0
6
1
9
Sum of Sames
22
8
16
4
Weighted Sum of Positives
0
33
19
37
Weighted Sum of Negatives
0
21
5
30

## Slide 23: Exercises
Parametric Analysis (Exercise 14.6-13)
Pugh Concept Selection (Exercises 14.6-14, 15)

## Slide 24: Some TRIZ Challenges
How can you fill chocolate bottles with thick syrup? Heating the syrup will melt the chocolate
  Inventive Hint: Do It Inversely
After forging, metal parts are cleaned with sand. The sand catches in crevices of the forged shape. How can the sand be removed?
  Inventive Hints: Do It Inversely, Change the Physical State.
10mm holes are to be drilled in a rubber hose. The hose is flexible and makes the hole spacing uneven.
  Inventive Hint: Change the Physical State.
A desert rover has large tires to roll over boulders, but tests indicate it has a danger of tipping. How can you prevent the rover from tipping?
  Inventive Hint: Use a “Matreshka” (dolls within dolls).