## Slide 1
-6
-4
-2
0
2
4
6
15.1 Reliability Concepts and Management
Sigma Quality Management

## Slide 2: Objectives
Be able to define and specify Reliability, Availability & Maintainability for a product or service
Be able to identify appropriate reliability assurance activities for a new product or service design project

## Slide 3: Terms and Definitions
TERM | DEFINITION
ITEM | Some "thing" for which reliability is a quality characteristic.
FUNCTION | The purpose of an item. What is the item supposed to do? The definition is simple, but determining the specific functions of an item may take some thought.
TIME | The length of time the item is supposed to perform its function. Time can be expressed as clock time, operating time, cycles, number of demands, or even linear distance. In general, the "best" unit of time should correlate to the stress that is placed on the item that will eventually be expected to fail the item.
ENVIRONMENT | The aggregate of all external and internal conditions either natural, man-made, or self-induced, that influences the performance, reliability or survival of an item.
SYSTEM | A composite of items, equipment, personnel and their associated skills and techniques capable of performing some function or mission.
PROBABILITY | For this text, the notion of relative frequency will be adopted as the definition of probability. That is, by performing an "experiment" many times, the relative frequency of some event (number of times the event occurs divided by the number of experiments) will converge to the probability of the event.
STATED CONDITIONS | The environmental conditions in which the item is expected to perform its function. Most generally, the conditions under which the customer will use the item.
MISSION | A specific task or operation for which the system's function, time and stated conditions are clearly defined. Note: Some systems will not have a "finite" mission. Utility distribution systems, for example, are expected to continuously supply electricity to the customer. It may be more useful to understand what constitutes a service interruption to the customer. This is usually a function of both power quality and continuity.
MISSION PHASES | When a system's configuration does not stay the same for the duration of the mission, phases are defined to help aid the reliability evaluation. A mission phase is a portion of the mission where the system's function is constant.
Page 15.1-3

## Slide 4: Reliability Definition and Measures
Reliability – Success/Attempts
Mean Time Between Failures (MTBF)
Mean Time To Failures (MTTF)
"The probability that an item will perform its intended function
under stated conditions for at least a given period of time."
Page 15.1-6

## Slide 5: Maintainability Definition & Measures
Mean Time to Repair (MTTR)
Mean Down Time (MDT)
Maximum Repair Time (MRT)
"The probability that a failed item will be repaired in a given time under stated conditions."
Page 15.1-7

## Slide 6: Availability Definition & Measures
Availability (A)
Availability (A) is the probability that a system is in an operable condition. In its simplest form, availability is expressed as the ratio of the total Uptime of a system to the total period time.
Page 15.1-8

## Slide 7: Failure Defined
A failure is an unsatisfactory condition.
A failure occurs when a product ceases to perform its expected function, under stated conditions, for an expected period of time.
Page 15.1-9

## Slide 8: Reliability Management
"The systematic activities that occur to assure that the reliability required by the consumer is met or exceeded."
Page 15.1-12

## Slide 9: Reliability Management Processes
President
or CEO
Vice President
Vice President
Vice President
Vice President
Vice President
Vice President
Vice President
Vice President
Vice President
Marketing and
Planning
Materials Mgmt.
Purchasing
Materials
Design
Construction &
Project Mgmt.
Maintenance
Operations
Production
Customer Needs Identified
Customer Needs
Met
Marketing & Planning
Design
Construction
Operations
Purchasing
Materials
Maintenance
Page 15.1-16

## Slide 10: New Product Development Process
Research
Phase
Concept
Development
Phase
Product/Process
Development &
Qualifications Phase
Production
Startup
Phase
Product Launch
& Support
Phase
Determine Customer
Q/R Requirements
Determine Application
Q/R Requirements
Perform Competitive
Q/R Analysis
Determine Feasibility
of meeting Q/R Requirements
Q/R Requirements
Reliability Data Analyses:
- Historical Field Failure Reports & Modes (FFRs)
- Competitive FFR’s & Modes
Installability, Serviceability
Safety Codes & Standards
Reliability Component Allocation
Supplier Selection
Quality Plan Established
Early (Prototype) Field Tests
Machine/Process Requirements, CpK 2.0
Risk Assessment - Rule Based
Robust Design
Accelerated/Abuse Life Testing
Key Qualification Requirements
-New Components
-New Processes
Prototype Evaluation
Reliability Prediction
Supplier Application Signoff
Machine/Process Specs,
PpK 1.3
Process FMEA
Key Characteristics
Performance Tests
Qualification Tests
Planned Field Tests
Manufacturing Sample Evaluation.
Machine/Process
Capability Studies
Pilot Run
- Mfg. Sys. Evaluation
- Quality Plan Evaluation
- Supplier Evaluation
- First Pass Yields 98%
Risk Assessment
- Rule Based
Resolve Lab/Field Failures
Customer PPM 500
Early Warning Analysis
Failure Rate/Mode Analysis
Reliability Improvements
Field Analysis Results
Quality Reviews/Controls
Supplier Reviews/Controls
In-Process Data Review
Machinery/Process Audits
Product Acceptance Tests
Lessons Learned
Page 15.1-23

## Slide 11: Exercises
RAM Concepts (Exercise 15.6-2)