## Slide 1
-6
-4
-2
0
2
4
6
15.2 Failure-Error Modes & Effects Analysis
Sigma Quality Management

## Slide 2: Objectives
Be able to identify, prioritize and identify countermeasures for important failure modes of a product or service
Ditto for important error modes of a human process

## Slide 3: Managing Reliability
To ensure the reliability of a system, we must manage the system's failures.
Page 15.2-2

## Slide 4: FMEA Purposes
Checking (and improving) the system's design as it exists on paper.
Identifying those critical components that required extensive testing to determine their reliability.
Planning the system's maintenance program to determine preventive and corrective maintenance actions.
Improving the reliability of existing systems by identifying, ranking, and improving critical components of systems or processes.
Page 15.2-2

## Slide 5: FMEA Example
Page 15.2-4

## Slide 6: FMEA Terms and Definitions
TERM | DEFINITION
Mission Profile | A description of the system's functions and the environments it experiences in all phases (start-up, operate at load, shut down), including criteria for performing the functions successfully.
Indenture Level | The level at which the system is being analyzed. Higher indenture levels represent a higher level of detail for the FMEA (i.e. to “lower” levels of the system). For a power plant, the indenture levels would proceed from unit (lowest), to system, to subsystem, to equipment, to component, to part (highest).
Failure Mode: | The ways in which the item can fail. For example, a relay's functions are to open and close upon demand (and stay open or closed). Failure modes could be: "fail to open", "fail to close," or "spurious transfer."
Failure Causes | The possible physical, chemical, electrical (and other) causes associated with each failure mode. For the relay's failure mode of "failure to open upon demand," the possible causes could include magnetized contacts, burred contacts, coil insulation failure, broken wire in coil, etc.
Failure Effect | The consequences of the failure mode on the operation or function of an item. Failure effects are classified as: Local effect, the consequence of the failure mode on the item being analyzed, Next higher level effect, the consequence the failure mode has on the next lower indenture level, End effect, the consequence the failure mode has on the lowest indenture level (i.e. system).
Failure Frequency | The expected rate of occurrence of the individual failure modes (how often the failure mode is predicted to occur).
Failure Severity | A quantitative measure of the effect of the failure mode. It is a relative measure of the worst potential effect of the failure mode.
Failure Detection | The means or methods by which a failure can be detected or predicted by an operator during normal system operation or can be detected by a maintenance crew by some diagnostic action.
Criticality Assessment | A procedure by which each failure mode is ranked with respect to the other failure modes to determine its criticality in the system. This is typically determined as a function of failure severity and failure frequency, but other factors, such as ease of detection, can also be included.
Page 15.2-5

## Slide 7: Functional Block Diagrams
FUNCTIONAL BLOCK DIAGRAM
- AIR COMPRESSOR
ELECTRICAL
CONTROL
POWER
480VAC
SALT TO FRESH
WATER
EXCHANGE
FRESH WATER
MOTOR
10
AUTOMATIC SHUTDOWN SIGNALS
(TEMPERATURE & OIL PRESSURE
INSTRUMENTS
& CONTROLS
20
TORQUE
(3510 RPM)
COMPRESSION
50
TEMP. & PRESSURE
READOUT
COOLING &
MOISTURE
SEPAR. (30)
LUBRICATION
40
COOLED OIL
COOLED
DRY
AIR
AIR PRESSURE RELIEF
SENSOR OUTPUTS
OIL
HIGH
PRESSURE
AIR
Page 15.2-6

## Slide 8: Reliability Block Diagrams
A
B
C
D
C1
C2
A
B
C1
D1
C2
D2
Series
Parallel
Series - Parallel
Page 15.2-7

## Slide 9: Component Identification
RELIABILITY BLOCK DIAGRAM
- AIR COMPRESSOR
MOTOR
10
INSTRUMENT
& CONTROLS
20
COOLING &
MOIST. SEPAR.
30
LUBRICATION
40
COMPRESSION
50
Page 15.2-8

## Slide 10: FMEA Procedure
Understand the System Functions
Subsystem
Function(s)
Success Criteria
Function Time
Environment
Fan
Provide directable
cooling air to electronic
equipment cabinets
No less than 200 cfm cooling air
No less than 2
hours
-
all
functions
Bounding conditions: 30F
120F, 100% RH,
M
otor
Transforms electrical energy
into shaft torque to turn fan
blade
"x" torque at "y" speed
Normal atmospheric
pressure, benign
Fan blade mounting system
Able to support fan weight,
startup & operating thrusts
Ground environment
Battery
Provide e
lectrical power to
fan circuit
Provide "m" amps at
"n" volts for a minimum of 2 hr.
Switch
Provides electrical continuity
(on demand)
Conduct "m" amps at "n" volts
Interrupts circuit (on demand)
Interrupt "m" amps at "n" volts
Allows selection
of “high” or
“low” speed or “off”
Switch circuit from “off” to “low”
to “high” and back to “off”
Wires
Provide electrical continuity,
transmit electrical energy
Conduct "m" amps at "n" volts
Battery
M
Fan
Switch
Resistor
Low
High
Page 15.2 10-12

## Slide 11: 2. Determine the Analysis Level of Detail
SYSTEM
EQUIPMENT
COMPONENTS
Two Speed
Portable Fan
10. Fan
11. Fan Blades
12. Fan Hub
13. Shaft Spline
20. Motor
21. Case
22. End Bells
23. Shaft
24. Bearings
25. Stator
26. Rotor
27. Collector Rings
28. Brushes
29. Leads
30. Batter
y
31. Case
32. Plates
33. Electrolyte
34. Terminals
40. Switch*
41. Contacts
-
High
42. Switch Pole
43. Terminals
44. Case
45. Contacts
-
Low
46. Resistor
50. Wires
51. Wire Segments
52. Wire Joints
Page 15.2 12-13

## Slide 12: 3. Develop the Functional Block Diagram
Battery
(30)
Switch (High Speed) (40)
Wires
(50)
Motor
(20)
Fan
(10)
Electrical
Energy
Electrical Continuity
Torque
Cooling Air
Page 15.2-14

## Slide 13: Develop the Reliability Block Diagram
Battery
(30)
Switch
(40)
Wires
(50)
Motor
(20)
Fan
(10)
Page 15.2-14

## Slide 14: 5. List the Function of the Item
Describes What The Item is Supposed to Do.
Function: Verb + Noun
Examples:
  Transmit Electrical Energy
  Provide Signal to Operator
  Convert Mechanical to Electrical Energy
  Form Staple on Blood Vessel
  Transect Abdominal Tissue
  Clean Teeth
  Maintain Pressure Integrity
Page 15.2-14

## Slide 15: 6. List the Failure Mode(s) of the Item
Premature Operation
Failure to Operate at a Prescribed Time/Condition
Intermittent Operation
Failure to Cease Operation at a Prescribed Time/Condition
Loss of Output or Failure during Operation
Degraded Output or Operational Capability
Describes the How, Not the Why
Page 15.2-15

## Slide 16: 7. List the Possible Causes of the Mode
Person
Method
Materials
Machine
Environment
Failure
Mode
Defective Material
Defective Processing
Defective Assembly
Fatigue
Assembly Flaws
Welding Flaws
Construction Flaws
High Temperature
Low Temperature
Humidity
Vi
bration
External Force
Contamination
Chemical Spray
Salt Spray
Mechanical Stress
Temperature Change
Pressure Change
Radiation (UV, Gamma, etc.)
Other Environmental Factor
Page 15.2-15

## Slide 17: 8. Determine the Effect of Each Failure Mode
What Happens When the Failure Mode Occurs
Local (i.e. Subsystem) versus Ultimate (i.e. System)
Page 15.2-16

## Slide 18: 9. Determine Detection Abilities
During Operation
During Construction/Manufacture
Page 15.2-17

## Slide 19: 10. Perform a Criticality Assessment
Risk Priority Number (RPN)
FAILURE PROBABILITY
SCORE
Failure is very unlikely to occur
1
-
2
Failure probability is low based on data from similar components
3
-
4
Possibility exists for failure to occur
5
-
6
Failure probability is high based on data from similar components
7
-
8
Failure is very likely to occur
9
-
10
FAILURE SEVERITY
SCORE
Minor failure that may pass unnoticed by the user
1
-
2
Minor failure that deteriorates item's appearance
3
-
4
Medium failure that causes functional deterioration during operation/use
5
-
6
Major failure that dis
ables operation/use
7
-
8
Critical safety failure resulting in injury or death, or damage to property
9
-
10
Page 15.2 17-18

## Slide 20: 10. Perform a Criticality Assessment
Risk Priority Number (RPN)
PROBABILITY OF FAILURE DETECTION
SCORE
Possible to detect almost every failure in
-
house prior to construction/assembly
(i.e. at receipt inspect
ion)
1
-
2
Mostly detectable prior to completion of construction/ maintenance. Usually
detected during assembly/fit
-
up
3
-
4
Undetectable until turnover to operations. Most failures detected during startup
or post
-
maintenance testing
5
-
6
Undetectabl
e until use by operations/end
-
user. Most failures detected during
operations/periodic testing
7
-
8
Undetectable until demanded by abnormal condition/ accident, not detectable
during operations/periodic testing.
9
-
10
Page 15.2-18

## Slide 21: 11. Recommend Corrective Actions
Mitigating Severity
Reducing Frequency of Failure
Improving Failure Detection
Page 15.2-17

## Slide 22: Process FMEA
Page 15.2-28

## Slide 23: Procedure
Understand Process Functions
Identify Process Level for Analysis
Develop Process Flowchart(s)
List the Process Step Being Analyzed
Identify Process Failure Mode/Error Modes
Determine Effect of Failure/Error on Process
List Possible Causes for Each Failure/Error Mode
Determine Failure/Error Mode Detectability
Determine Criticality of Failure Modes
Process Improvement Recommendations
Page 15.2-32

## Slide 24: Error Proofing Approaches and Examples
I. Prevent Errors
A. Eliminate the possibility of the error
  Lawn mower must have safety bar engaged to start engine
  Gas cap tethered to car so it cannot be left behind
B. Delegate decisions
  Cash register calculates change
  One-touch setting for popcorn on a microwave
C. Facilitate tasks
  Program VCR using a program code
  Wires that connect are color coded
II. Mitigate Errors
A. Detect Errors
  Auto-shut off on coffeemakers and irons
  Spell checking in word processor
B. Mitigate Errors
  Radar for collision avoidance
  Automatic correction of spelling errors in a word processor
Page 15.2-36
Notes: This model of ways to error proof is derived from: The principles of foolproofing and their application in manufacturing.
Nakajo, T. and Kume, H. 1985. Reports of Statistical Application Research, Union
of Japanese Scientists and Engineers 32(2): 10-29.

## Slide 25: Clearing Copy Jams
Copier Jams
Open Copier Door
Look in Paper
Tray Outlet
Restart Job
Pull Paper
Out, Close
Door
Call Tech
Found?
More Jams?
Finish Job
Found?
Look in Fuser
Area
Found?
Look in
Collater Area
Found?
Look in Drum
Area
No
Yes
No
No
No
Yes
Yes
Yes
Yes
No
Page 15.2-38

## Slide 26: Process FMEA
Page 15.2-39

## Slide 27: Exercises
Home AC Unit FMEA (Exercise 15.6-4)
Home AC Unit EMEA (Exercise 15.6-5)
Perform an FMEA:
  To Analyze What Can Go Wrong in Your Process
  To Assess the Risk of the Change You are Planning for Your Process