## Slide 1
-6
-4
-2
0
2
4
6
15.3 Fault Tree Analysis
Sigma Quality Management

## Slide 2: Objectives
Identify potential failure modes/root causes of product or process performance requirements using Fault Trees
Predict the reliability of a new or redesigned product or process

## Slide 3: Fault Tree Purposes
Fault Tree analysis (FTA) can yield both qualitative and quantitative information about the system.
FTA provides a better understanding of potential design problem areas and gives the designer a chance to improve the design at a less costly stage of the product's lifecycle.
Fault Tree Analysis has been used to aid in uncovering the root cause(s) of important failures.
Fault Trees prepared ahead of time have been used as diagnostic tools, enabling the operations and maintenance forces to quickly zero-in on the cause of a problem.
Fault Trees have also been used to evaluate existing systems (typically safety systems) to determine if these systems are vulnerable to "hidden" failures not found through other design checks. This versatile tool has also been used to examine the impact of proposed modifications to a system.
Page 15.3-2

## Slide 4: Example Fault Tree
Mechanical Pump Seal
Cooling Water
Pump Seal
Failure
Primary Seal
Failure
Secondary
Seal
Failure
Loss of
Cooling
to Seal
Loss of
to Seal
O
-
Ring
Failure
Excess
Pump
Vibration
Thrust
Bearing
Misaligned
Carbon
Face
Failure
Carbon
Face
Wear
Wear
O
-
Ring
Cooling
Improper
Installation
Page 15.3-3

## Slide 5: Fault Tree – Building Blocks
AND
OUTPUT
INPUTS
OR
OUTPUT
INPUTS
INPUTS
OUTPUT
A
B
C
Occurs
Occurs
Occurs
Occurs
Does Not Occur
Does Not Occur
Does Not Occur
Occurs
Does Not Occur
Does Not Occur
Does Not Occur
Does Not Occur
INPUTS
OUTPUT
A
B
C
Occurs
Occurs
Occurs
Occurs
Does Not Oc
cur
Occurs
Does Not Occur
Occurs
Occurs
Does Not Occur
Does Not Occur
Does Not Occur
Page 15.3-4

## Slide 6: Inhibit Gate
Page 15.3-5
Fire
Fuel
Leak
Oxygen
Spark

## Slide 7: Event Types
The
Basic Event
, represented by a circle, describes a basic initiating fault event
that cannot be developed further or a basic event in the lowest level whose
probability of occurrence can b
e obtained independently.
The
Undeveloped Event
, represented by a diamond, describes fault events that
are not further developed, either because the event is of insufficient consequence
or because of the lack of necess
ary information. In order to obtain a solution for the
Fault Tree, both circles and diamonds must be represented by probabilities of
failure.
The
External or House Event
is used to describe events that are normally
exp
ected to occur and are generally not “faults.” For example, the presence of
oxygen in the analysis of a fire could be a House Event.
Page 15.3-6

## Slide 8: Other Event Types
The Intermediate Event
Transfer Events
IN
IN
Page 15.3-6-7

## Slide 9: Relationship to Boolean Algebra
Logic Diagram vs. Algebraic Expression
Equivalence of the Tree to Logic Expression
Equivalence of Logic Expression to Probability Expression
Page 15.3-7

## Slide 10: Construction Steps
Examine the System to Be Analyzed
Define the Undesired (Top) Event
Establish the Analysis Boundaries
List the Sub-Events
Connect Sub-Events to Top Event
Continue the Analysis
Qualitative Analysis
Fault Tree Reduction/Simplification
Quantitative Analysis
Page 15.3 12-22

## Slide 11: Boolean Algebra “Rules”
Designation
Symbolism
Commutative Law
X
Y
Y
X
X
Y
Y
X
´
=
´
+
=
+
Associative Law
X
Y
Z
X
Y
Z
´
´
=
´
´
(
)
(
)
Distributive Law
X
Y
Z
X
Y
X
Z
´
+
=
´
+
´
(
)
Idempotent Law
X
X
X
X
X
X
´
=
+
=
Law of Absorption
X
X
Y
X
X
X
Y
X
´
+
=
+
´
=
(
)
Complementation
X
X
X
X
´
¢
=
+
¢
=
F
W
(The Nul
l Set)
(The Uni
verse)
deMorgan’s Theorem
(
)
(
)
X
Y
X
Y
X
Y
X
Y
´
¢
=
¢
+
¢
+
¢
=
¢
´
¢
Unnamed, but
frequently used
relationships
X
X
Y
X
Y
X
X
Y
X
Y
X
Y
+
¢
´
=
+
¢
´
+
¢
=
¢
´
¢
=
+
¢
(
)
(
)
Page 15.3-20

## Slide 12: Example System
Primary Makeup
System
Tank
Pump "A"
Pump "B"
Injection Line "A"
Injection Line "B"
Page 15.3-14

## Slide 13: Fault Tree - Skeleton
Page 15.3-16

## Slide 14: Exercises
Take One of Your CTQs – Develop and Quantify A Fault Tree with the CTQ as the Top Event
Home AC Fault Tree (Exercise 15.6-6)