## Slide 1
-6
-4
-2
0
2
4
6
Lean Manufacturing
Six Sigma Alliance, LLC
6
s

## Slide 2: What is “Lean”
“Lean” is a term used to refer to the processes, philosophy and improvement techniques that are proven to be the best in the world for delivering products and services.
“Lean” enterprises:
  are the most efficient (cost and working capital)
  have the highest quality (defects/million)
  are the most responsive to their customers (time, service and product development).

## Slide 3: Principles of Lean
While there is several schools of Lean manufacturing, these principles seem to be the basis for all.
  1. Identify Value Stream
  2. One Piece Flow
  3. Demand Pull
  4. Perfection

## Slide 4: The Value Stream
Taiichi Ohno found the modern supermarket so stimulating that it inspired him in 1950 to invent the new system of flow management we now call Just in Time.
Value stream:
  activities necessary to create, order, and produce specific products. Those which can't be precisely identified, analyzed, and linked together cannot be challenged, improved and, eventually, perfected.
  must manage the whole value stream for specific goods and services.

## Slide 5: Value Stream
Must define value stream in terms of the entire product not just one element of the product. Waste must be removed from the entire system in order to deliver the right product at the right time for the right price to the Customer better than the Competition.
For example:
  think of all the elements in different segments required to take a family vacation to another country.
  where would the major costs and time be incurred in producing and delivering a can of a soft drink to the Consumer?
Notes: Ask the group to think about and offer opinions as to the key Value Stream drivers in taking a vacation to another country.
Do the same with the soft drink example, then turn to the next slide.

## Slide 6: Value Stream
Identifying every action required to design, order, the make a specific product is to sort these actions in three categories:
  1. those which clearly and unquestionably create value as perceived by the customer;
  2. those which create no value but are currently required by the product development, order filling, or production systems and cannot be eliminated;
  3. those actions which don't create value as perceived by the customer and can be eliminated immediately.

## Slide 7: Tesco
An example given of the value stream is the life-cycle of a carton of cola. The cumulative days from mining the bauxite to making the aluminum can through consumption by the consumer, is 319 days. Total processing time is approximately three hours. Average consumption time is 5 minutes.
Notes: In the Lean Thinking book, the can of soda example is cited to show that the most time and expense by far is incurred from mining the ore to producing the aluminum can. If the soft drink manufacturer were to look only within the four walls of the bottling plants, very little of the Value Chain would be seen

## Slide 8: Tesco
The root cause of muda in the cola example is that all the apparatus used to make cola and get it to the customer is very large, very hard to changeover, and designed to operate efficiently at very high speeds. It is a mass production psychology. However, what appears to be efficient to individual companies, individual elements of the value chain, are far from efficient when viewed in terms of the total product and the total value stream.
Notes: In the Lean Thinking book, the can of soda example is cited to show that the most time and expense by far is incurred from mining the ore to producing the aluminum can. If the soft drink manufacturer were to look only within the four walls of the bottling plants, very little of the Value Chain would be seen

## Slide 9: Tesco
Tesco took the following steps to remodel this situation:
  Point-of-sale bar code scanning system in checkout lanes of all stores
  Transfer purchasing from individual stores to a centralized system to place combined orders from all stores with suppliers
  Implement regional distribution centers (large trucks in, large trucks out)
  Move to daily orders rather than weekly or monthly orders
Notes: In the Lean Thinking book, the can of soda example is cited to show that the most time and expense by far is incurred from mining the ore to producing the aluminum can. If the soft drink manufacturer were to look only within the four walls of the bottling plants, very little of the Value Chain would be seen

## Slide 10: Value Stream: Activities
There are three categories of activities generally associated with the Value Stream
  - problem-solving task (design to launch)
  - information management task (order taking to delivery)
  - transformation task (raw material to finished product with Customer)

## Slide 11: Some Advice...
To hell with Competition; compete against perfection by identifying all activities that are muda and eliminating them.
This is an absolute rather than a relative standard which can provide the essential North Star for any organization.
However, to put this mission to work a company must master the key techniques for limiting muda.
It all begins with flow.
Notes: Ask why it all begins with flow.
To master flow means that information and material proceed without stop or delay. Waste has been eliminated.
Then ask, “Is cost a cause or an effect (of how we choose to manage workflow)?”
Cost is an effect, a result. We can not manage results. We can only manage the causes that produce the results.

## Slide 12: One Piece Flow
One Piece Flow is the elimination of batch and queue work flows or reduced elapsed cycle time in environments in which batching is required, for example, under FDA regulation
Flow is counter intuitive.
People naturally tend to think in terms of batch processes. However, the move to flow should be not only in special cases, like the Ford assembly line, but in a general case, like small lot production in modern automobile assembly plants.

## Slide 13: One Piece Flow vs. Reengineering
The reengineering movement has recognized that departmentalized thinking is suboptimal and has tried to shift focus from organizational categories (department) to value creating "processes".
The problem is that the engineers haven't gone far enough conceptually. They are still dealing with disconnected and aggregated processes (for example, order taking for a whole range of products) rather than entire flow of value creating activities for specific products.
Kaikaku: radical improvement
Kaizen: continuous incremental improvement

## Slide 14: One Piece Flow in Production
Based on years of benchmarking,observation and implementation in organizations around world, we have developed the following simple conclusion about the application of these concepts and tools:
  converting the classic batch and queue production system to continuous flow with effective pull by the customer will deliver double labor productivity while cutting production throughput times by 90 percent and reducing inventories in system by 90 percent as well.
  Time to market for new products will be half and, within product families, a wider variety products can be offered at a very modest additional cost. What's more, the capital investment required will be minimal, even negative, the facilities equipment can be freed up and sold.

## Slide 15: One Piece Flow
Once Value is defined and the entire Value Stream is identified, we must simultaneously:
  1. Focus on the actual object (specific design, specific order, the product itself) from beginning to completion
  2. Ignore traditional boundaries of jobs, careers, functions
  3. Rethink specific work practices and tools to eliminate back flows, scrap, and stoppages of all sorts so that the design, order and production of the specific product proceeds continuously.

## Slide 16: Demand Pull
Demand is the Customer signal
Pull is the material signal
Then, Demand Pull, in the simplest terms, means that no one upstream should produce a good or service until the customer downstream tasks for it.
In essence, Demand Pull is a permission system that prevents waste of resources and material while accelerating flow and simplifying control

## Slide 17: Perfection
Once the other three elements of Lean are deployed and implemented, then the idea of achieving Perfection becomes quite defined and practical.
  Value stream identification
  One Piece Flow
  Demand Pull
  Perfection

## Slide 18: Exercise
Do an exercise that demonstrates the reduction in WIP and lead time and defects.
Start with a batching process
Then go to one piece flow
Then go to pull system.
Measure WIP
Lead time
Defectcs

## Slide 19: Lean Production Practices
Just in time techniques are used in the lean production environment, for example:
  Line leveling (heijunka)
  Changeover reduction (leverage to smaller, much smaller, batches)
  Reorganized operations into process related families
  One piece flow
  Right sized equipment (remember, determined in design process not just doing the best with what you have available)
  Elimination of the muda of complexity (all the undue operational overhead)
  Flexible and process trained workforce
  Robust and repeatable processes
  Dependable equipment (preventive maintenance, process capability)
  Standard work
  Mistake proofing (poka yoke)
  Autonomation
  Visual controls and the 5 Ss
  Takt time and quick changeover
  Demand pull system (permission system
  Pointed use delivery and storage of material
  The location of production and support resources (don't get stuff from East Wherever because it is a to few cents a unit cheaper)

## Slide 20: MUDA
Muda: the Japanese word for waste. It means any human activity which absorbs resources and creates no value.
There are seven traditionally described forms of waste:
    1. Excess Production
    2. Waiting
    3. Conveyance
    4. Unnecessary processing
    5. Inventory
    6. Unnecessary Motion
    7. Producing Failures
Notes: Remind group that “value” is defined by the Customer -- not the production process. It is not a value added operation to a cost standard.
Value is that for which the Customer is willing to pay.

## Slide 21: Reason For the 5S’s
Process Driven Organization
Elimination of Waste in the Process
  Waiting
  Conveyance
  Unnecessary Motion
Safer, High Quality Work Place Environment
Notes: What is a process driven organization? (One in which human activities are focused on managing and improving well defined, standardized, robust processes -- in both production and information flow)
How many types wastes are there in a JIT approach? (Seven wastes:
1.Excess Production
2.Waiting
3. Conveyance
4.Unnecessary processing
5. Inventory
6. Unnecessary Motion
7. Producing Failures
What waste does Lean add? 8. Producing goods and services that don't meet customer needs

## Slide 22: 5 S’s
1. Sort
2. Set in Order
3. Shine
4. Standardize
5. Sustain
Notes: Note that we will see that the first two, sort and set in order, are the most important of the 5 S's.
However, also note that without Sustain, the whole thing will fall apart.
Lastly, note that the approaches and techniques that will be discussed are applicable in all work flow environments; production, information flow, administration and clerical.

## Slide 23: 1. Sort
Remove from the Work Area All Items Not Required for Current Work Flow Activities
When in doubt, throw it out!
Notes: Why throw it out? Engage the class is a short discussion.
If it is a process driven organization, then the waste caused by clutter and unneeded items devalue the process. For example, the process should define and describe exactly what is needed to perform particular tasks and activities. That is all that is needed.

## Slide 24: 1. Sort: Red Tag Process
In a Target Area:
Identify Items of Questionable Need:
  Is the Item Required?
  Is the Item Required in the Quantity On Hand?
  If Required, Must It Be Placed/Stored Here?
Disposition Identified Items:
  Hold
  Relocate
  Dispose
  Leave in Place

## Slide 25: 1. Sort: Red Tag Process
1. Establish Red Tag Criteria:
  Usefulness
  Frequency of Use
  Quantity
2. Tag All Questionable Items
  Material/Equipment/Tooling
  Space
3. Move to Hold Area:
  Local
  Central
4. Evaluate & Disposition Red Tag Items
5. Log & Report Results
Notes: Note that tagged items can be things or space. For example, if shelving is being used to store unneeded material/tools, then the shelving space should be tagged along with the material/tools. Nothing should be sacred or overlooked.
Local Hold: way station for items to be moved to Central Hold; items that can be dispositioned by local authority; items "tested" for red tagging by holding for a predetermined period of time; etc...
Central Hold: for items that local management does not have authority to disposition; to meet audit/accounting requirements; for determination of distribution to other areas with need in the organization; to consolidate disposition efforts; etc...
Rem: Disposition could be: dispose, move, leave

## Slide 26: 2. Set In Order
Identify, Label and Arrange Required Items so that They Are Easy to Retrieve and to Store as Part of Routine Work Flow Process
When Set in Order Is Correctly Implemented, These Activities Can Be Performed by Anyone.
Notes: Rem: the process should be as simple as possible. Anyone should be able to easily locate and put away required items -- even those of similar appearance.

## Slide 27: 2. Set In Order: Method
Set In Order Uses a Two Step Method:
  1. Determine Appropriate Locations for
    Equipment
    Fixtures & Tooling
    Material
  2. Label & Identify Locations
Notes: Refer participants to appendices: principles of eliminating wasted motion; principles of storing jigs, fixtures, etc...
You may wish to moderate a brief discussion with the class.

## Slide 28: 2. Set In Order: Method
1. Determine Appropriate Location:
  Flow Map Current (Before) Work Flow (Spaghetti Diagram)
  Determine Improved Flow
  Detail Layout of Improved (After) Flow:
    Equipment
    Benches, tables
    Material & Space
    Tooling, fixtures
    etc...

## Slide 29: 2. Set In Order: Methods
2. Label and Identify Locations
  Visual Controls Communicate Simply and Quickly to Anyone the Standards by which a Task or Activity Should Be Performed
  Examples:
    Labeled and Outlined Tool Kit Boards & Tools
    Painting
    Sized Containers
    Color Codes
    Etc...

## Slide 30: 3. Shine
Keep the Work Place Clean and Clutter Free
Insure that Anything Needed Will Always Be Ready When it Is Needed
Reinforce with Inspection

## Slide 31: 3. Shine: Methods
1. Identify Shine Targets:
  Warehouse/Stockroom Items
  Equipment
  Space
2. Assign Shine Responsibilities & Schedule
3. Standardize/Document Methods & Measurements
4. Prepare Tools & Training
5. Implement & Follow-up
Notes: Ask participants how often should inspections be performed? Moderate the discussion if there is a difference of opinion. Ultimately, the participants should realize that the statement of measurements and the inspection should happen at least on every shift. This should be a routine part of the work process.

## Slide 32: 4. Standardize
The Result that Exists When Sort, Set in Order and Shine Are Properly Maintained
Standardization Insures that These Daily Work Habits Are Fostered and Maintained Completely, Fully and Productively

## Slide 33: 4. Standardize: Methods
1. Determine Responsibilities:
  Operator
  Supervision
  Maintenance
  Other
2. Integrate in Routine Work Activities
3. Follow-up and Track Routinely

## Slide 34: 4. Standardize: Tools
Change Job Descriptions
Visual Plant
Charts
Work Aide Sheets
Checklists
Etc...

## Slide 35: 4. Standardization: Prevention
If the Standard Process Is Being Followed Correctly But Waste Continues:
  Ask “Why” Until Root Cause is Identified (Ask Why 5 Times)
  Ask “How” Can This Be Fixed
  Implement Change to Standard

## Slide 36: 4. Standardization: Prevention
Prevention Example:
Waste: Operators need to sweep floor in addition to cleaning machine table of chips and shavings from drill press operations
Prevention: Place metal and plexiglass panel to prevent chips and shavings from falling from machine table to floor.

## Slide 37: 5. Sustain
Habit of Properly Maintaining Correct Procedures is Internalized by the Organization.
Different from Standardize in that Sustain Can Not Be Measured or Are Results Visible -- it Is Changed Behavior
Sustain Takes Leadership and Time to Achieve

## Slide 38: Traditional manufacturing layout
Stock-
room
1 Turning
4 Grinding
3 Milling
2 Drilling
Customer

## Slide 39: Why Redesign Process Flow?
As much as 60% of the total labor can be expended on non-value adding activities such as
  Moving, counting and storing WIP
  Unnecessary Inspection
  Equipment attend
To eliminate these non-value adding and wasted activities, redesign the process flow and organize the equipment into cells
  Parts are moved and processed in small batches (ideally batch size of 1) uninterrupted from one operation to another
  Having equipment in a linear flow forces problems to surface so that they can quickly be solved

## Slide 40: Cell Design Overview
  Organizing cells around families of similar products
  Organizing the equipment for each step to minimize part travel
  Eliminating any non-value added steps
  Collapsing the sequence of cell operations so that the output of one step feeds the next
  Avoiding barriers that prevent visibility of all cell operations
  Using the absolute minimum amount of space required for machines, tools, operators and inventory
Input
=
Process
(1)
Process
(2)
Input
Output
Output
Single unit flow -- Transfer Batch
Focused Factory Cell
SmallProcess Batch

## Slide 41: Cell Design Overview
Currently mfg and assy processes are organized in a functional layout
  Organized by individual process step
  Separated by long travel distances
  Inventory storage locations prior to each step
Input
Inventory
In-Bay
Process
(1)
Process
(2)
Input
Output
Output
Output
Work Center 23
Work Center 48

## Slide 42: Process Redesign Benefits
Reduces Cycle Time
Increases throughput (not more)
Allows responsiveness to changes in demand
Promotes high visibility of the process
Gives operators immediate feedback
Improves quality
Minimizes travel distances, material handling, and space
Anticipate equipment performance (i.e.. minimize unplanned downtime)
Increase process ownership by operators

## Slide 43: Process Simplification
“To-Be” Process
“As–Is Flow”
“To-Be Flow”
Group product information process families when redesigning the process,
  Takt time
  Eliminate non– value added activities
  Increase organizational spans of control
  Reduce the number of decision points
  Increase yields
  Simplify and streamline the process
  Incorporate board room management
  Separate operator time from machine time
  Train “one-ups, one-down”
Eliminate
Non–Value
Added
Activities

## Slide 44: Cellular Processing Manufacturing
1 Turn 2 Drill 3 Mill 4 Grind
1 Turn 2 Drill 3 Mill 4 Grind
• One-At-A-Time/First-In-First Out
• Synchronous To Demand (Demand Pull
• One Operator-Multiple Machines
• Immediate Feedback
• Standard Work-in-Progress
• Small Lot Process Batch
• One Piece Transfer Batch
“To Be” Layout

## Slide 45: Challenge the Process
Press
Primary
Form
Queue
Wash
Store
Press Final
Form & Trim
Queue
Fabricate Governor Hsg
Fabricate Exit Device Cover
Assembly
Final
Form
Pierce
Bolt
Hole
Drill &
Count-ersink
Flatten Bill of Materials
Simplify / Streamline Processes

## Slide 46: Cell Design Overview
In cases where multiple cells feed one another, the design layout must include visible storage area for kanban inventory and pull signal communication
A
A
B
B
C
C
D
D
D
D
E
E
E
E
Final Assembly Cell
Final Assembly Process
Step
1
Step
2
Step
3
Step
4
Single unit flow
Output
Sub-assembly Cell 1
Input
=
Process
(1)
Process
(2)
Input
Output
Output
Single unit flow
Sub-assembly Cell 2
Input
=
Process
(1)
Process
(2)
Input
Output
Output
Single unit flow

## Slide 47: Examples of cell layouts
U - shaped
S - shaped
Line
Mixed

## Slide 48: Desirable Characteristics of Cells
Material passed right-to-left
No conveyers, belts, rollers
Visibility and feedback are maximized
Standard WIP
Set inspect points
Staffing flexibility and satisfaction maximized
Equipment
Workflow
Replenishable
materials
Tools, gauges,
supplies

## Slide 49: Principles of Cell Design - operators
Keep the operator inside the cell, with benches, machines, and material presentation on the outside
Place operators close together
Keep the distance between an operator and part travel to a minimum
Don’t isolate operators
Separate operator time from machine time
Better: Operators can help each other. Might increase output with third operator.
BAD: Operators bird caged. No chance to increase output with a third operator.
Material

## Slide 50: Cell Design Considerations
Material Flow
Better: Operators can trade elements of work. Can add and subtract operators. Trained ones can neatly self-balance at different output rates.
BAD: Operators caged. No chance to trade elements of work between them. (Subassembly line layout common in American plants)
Material Flow

## Slide 51: Principles of Cell Design
Don’t isolate equipment
Make machines movable where practical
  Have machines on wheels (on air pallets) for ease of maintenance and cell fine tuning
Don’t be trapped by “machine utilization”
Make waste visible
The operators and the part do not have to travel the same path
Place functionality above appearance; cell designs can be “ugly”

## Slide 52: Cell Design Considerations - material flow
Make working conditions easy, avoid ladders, use platforms or cut holes in the floor for easy access to equipment or product
Standardize table/work station height
Avoid unloading an operation to a table then reloading to the second operation
  Feed the output of one operation directly to the second operation
  Have the operator unload the previous operation
  Automate unload
Eliminate conveyors
To conveyorize is to institutionalize
STN 1
STN 2
STN 3
STN 4

## Slide 53: Housekeeping
Make housekeeping an easy part of maintaining cell operations
A place for everything and everything in its place
Push responsibility throughout the organization
Provide guidelines
Specific areas include:
  scrap area / disposal procedures
  tool storage on outlined peg boards
  machines cleaned / painted
  lines labeled
  storage designated

## Slide 54: Cell Operating Principles
Stop the line when imbalances occur
If a cell stops—solve the problem, don’t keep people busy making inventory
First, eliminate the cost (non-value) adds, then streamline the value adds
Stress the cell! When shift production is regularly completed before shift end, reassign an employee and rebalance the cell

## Slide 55: Expected Results
Housekeeping
Quality
Operator Satisfaction
Machine Reliability
Good cell layout and process discipline form the foundation of performance improvement
Cycle Time
Inventory
Product Cost
Process Variability

## Slide 56: Visual Controls
Visual Controls Communicate Simply and Quickly to Anyone the Standards by which a Task or Activity Should Be Performed in any Work Flow Environment

## Slide 57: Visual Controls
A well implemented Visual Control System:
  passes decision-making to the point of operation
  prevents mistakes
  quickly highlights mistakes or variances that have occurred

## Slide 58: Visual Controls
Examples of Common Visual Controls Systems are:
    Kanbans Cards and Kanban Squares
    Schedule Boards
    Labeled and Outlined Tools & Tool Kit Boards
    Painting
    First-in-First-Out Queues
    Dedicated, Sized Containers
    Color Codes
    Etc...

## Slide 59
Finished Goods Replenishment Unit Kanban Board
RED
GREEN
YELLOW
Kanban in RED ZONE triggers Renewal
- Production Problem?
- Unexpected Demand Increase?
Kanban in GREEN ZONE continue according to plan
Kanban only in YELLOW ZONE triggers Renewal
- Unexpected Demand Drop?
- Unexpected Capacity?

## Slide 60: Paint
Aisle/Walkway
Material Storage
Material Storage
Before

## Slide 61: Paint
After
Aisle/Walkway

## Slide 62: Schedule Board

## Slide 63: Set-Up Time Reduction Benefits
More frequent changes . . . allow
Shorter production cycles . . . which
Lower inventories . . . and offer
More flexibility . . . to deliver
Faster customer response . . . with
Better quality . . . resulting in
Higher controllable earnings
Decreased set-up time provides a stream of benefits . . .
Notes: Set-up improvement will accomplish two things:
1. Reduction of waste of people, equipment and, possibly, material.
2. Improved competitive position.
What is one way that set-up improvement can improve competitive position? Go to next slide

## Slide 64
Old Batched Lots
New Small Lots
Assembly Schedule
DAY
ITEM
1 2 3 - - - - - 30
A
B
C
D
Assembly Schedule
DAY
ITEM
1 2 3 - - - - - 30
A
B
C
D
Sell Daily? Build Daily!
Reducing Lot Sizes is Critical to Being Able to Produce to Customer Demand and Respond Flexibly
Set Up Time = One Piece Flow

## Slide 65
Greatly Increase Flexibility By Affording the Opportunity to Reduce Lot Sizes
The number of different lots produced is increased in direct relation to shortening set-up time (e.g., 5 times as many different parts produced equates to the individual set-up being allowed 1/5 the time.)
Total Required Hours
Production Time
Set-up Time
Production Time
Production Time
Set-up
Time
Set-up Time
Part “1”
Part “2”
Part “1”
Part “2”
Part “3”
Part “4”
Part “5”
Part “6”
Part “7”
Part “8”
Part “9”
Part “10”
Set Up Time Reduction

## Slide 66: Set-up Time Reduction 12-Step Process
1. Create Team
2. Select Set-up Project
3. Determine Set-up Time Reduction Goal
4. Videotape Set-up Activity
5. Document Activities
6. Identify Internal vs. External Elements
7. Housekeeping/Organization
8. Shift Internal to External
9. Improve Elemental Operations
10. Standardize and Document New Methods
11. Analyze New Method & Videotape
12. Goal Attained

## Slide 67: Overview: Mistake Proofing (Poka-Yoke)
A Lean Enterprise is a process driven enterprise that is always striving to eliminate waste
Processes should support the perfect satisfaction of Customer requirements when followed correctly
Mistake Proofing is a method for insuring that the process is necessarily followed

## Slide 68: Overview: Defect Causes
Most defects are caused by Human Error, such as (in order of importance):
  1. Omitted Processing
  2. Processing Errors
  3. Errors Setting Up Workpieces
  4. Missing Parts
  5. Wrong Parts
  6. Processing Wrong Workpiece
  7. Misoperation
  8. Adjustment Error
  9. Equipment Not Set Up Properly
  10. Tools and Jigs Improperly Prepared

## Slide 69: Overview: Poka-Yoke
Poka-Yoke: loosely translated means “mistake proofing”. It is from Japanese:
  yokeru: to avoid
  poka: inadvertent errors
Key Attributes:
  Respect for Worker Intelligence
  Focus on Repetitive Activities that Rely on Vigilance and Memory
  Free Worker to Pursue Creative, Value-Added Activities

## Slide 70: Quality Control Techniques
There are three categories of inspection approaches:
1. Judgement Inspection
2. Informative Inspection
3. Source Inspection

## Slide 71: Judgement Inspection
Approach: Focus on preventing “escape” defects from getting to the Customer by inspection and separation of good product from bad product after processing
Result: Escapes are prevented but Defect Rate is not reduced.

## Slide 72: Informative Inspection
Approach: Investigate “cause” of defect and reports this information so that the process can be improved to further reduce defects
Result: Tolerates, a priori, existence of defects

## Slide 73: Source Inspection
Approach: 100% Inspection at Source Activity so that simple “mistakes” can be prevented prior to generating a defect
Result: Mistakes are prevented through Mistake Proofing (Poka-Yoke) providing Zero Quality Control

## Slide 74: Zero Quality Control
Three Components:
  Source Inspection: errors, not defects
  100% Inspection: inspection simple, inexpensive and automatic part of process
  Immediate Action: stop the process

## Slide 75: Zero Quality Control
Strategies for Zero Defects:
  1. Don’t make it if it isn’t needed
  2. Make it to withstand any use (don’t let the Customer be your inspector)
  3. Make it, use it immediately (small lot/continuous flow production)

## Slide 76: Mistake Proofing
Defects occur when there is a breakdown in one or more of the Five Elements of Work Flow:
  1. Associate/Operator
  2. Material
  3. Equipment
  4. Method(s)
  5. Information

## Slide 77: Mistake Proofing: Defects
Defects can exist in one of two states:
  Defect has occurred
  Defect is about to occur

## Slide 78: Mistake Proofing: Defects
Mistake Proofing has three functions used when Defects are Predicted or Detected:
  Shutdown
  Control
  Warning

## Slide 79: Mistake Proofing
Mistake Proofing, in general, is:
  Simple
  Quick to Implement
  Inexpensive or free

## Slide 80: Mistake Proofing: Eight Principles
1. Build quality into the process
2. All inadvertent errors can be eliminated
3. Stop doing it wrong,Start doing it right-now
4. Don’t think “Why I can’t do it right”, think “How can I do it right?”
5. Go for a 60% chance of success
6. Team work can reduce mistakes and defects to zero
7. Ten heads are better than one
8. Ask “Why” 5 times and “How” once (5W’s & 1H) to isolate root cause.

## Slide 81: Common Mistake Proofing
Several of the most common methods used for mistake proofing are:
  Guide pins of different sizes: interference fits
  Error detection and alarms
  Limit switches
  Counters
  Checklists