## Slide 1: Pull System
Notes: We’re going to talk about the pull system; we’re going to define it, discuss the objectives and give some examples of pull systems in use.
Then we’re going to discuss traditional systems and how they contrast with a pull system.
Next we’re going to investigate how a pull system is managed, what types of pull signals could be used and why you would want to use a particular kind.
We’ll close the discussion by looking at the benefits that can be achieved by implementing a pull system.
Note: this group of slides contains some that may not be appropriate for the workshop discussions. Use the material as you see find it fits the situation.
Key points of Pull Module:
Possibilities in all areas: administrative, indirect, direct
Simplicity of various types
Sends a visual message
Operator control, does not require management involvement or sophisticated systems.
Must have discipline.
Exists in our lives everywhere but work.

## Slide 2: Pull System
Definition:
A method of controlling the
flow of resources by
replacing only what has
been consumed.
Pull Signals
Pull Process
Material At
Operator
Manpower
WASTE
Notes: Before showing slide, ask question: how would you define a pull system?”
After obtaining some responses show slide. Emphasize the underlined words as key aspects of what pull is all about.
Note that a pull system is closed loop and brings together the operator with the rest of the material supply system.

## Slide 3: Push System
Definition:
Resources are provided to
the consumer based on
forecasts or schedules.
Notes: Conversely, a definition of the push system is reflected on this transparency.
Ask the group how accurate are forecasts or schedules? Despite the best computers and programs, schedules vary from actual demand because they are our best guess, not actual demand or consumption.

## Slide 4: The Material Dilemma
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
Looking
for Parts
High
Inventory
Counting
Parts
Moving
Parts Long
Distances
Notes: Thus, in a traditional push system we have a material dilemma:
High inventories are common because we anticipate the material required by our customer who can not always build to schedule.
Counting parts is burdensome and time consuming. Quantities often vary from container to container.
Parts are often stored in different locations and inventories disappear (shrinkage).
Transport time due to different storage locations increases lead time.

## Slide 5: The Toilet Paper Analogy
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
TP
Notes: If we applied the materials logic we use on the factory floor to our homes, our homes would look like this. What is wrong with this house?
Would you build an addition on your house just to store toilet paper if you could get a bargain from a supplier if it was bought in large volume? Of course not! As consumers, we demand goods in a reasonable quantity and at an affordable price.
Do the rooms in this house appear normal to you? Would you organize your house in this manner? Notice everything is out of place. At home, we organize things for our convenience so we can be more efficient, save time and energy. Why don’t we do this at work?
Our material dilemma forces us to store parts where they don’t belong because of the high inventories. Thus, making parts hard to find, hard to count, and moving them long distances.
Workplace organization and visual controls provide the tools we need to solve these problems.

## Slide 6: Customer Pull
• Requirements
- Fresh
- Available
- Brand
- Price
- Size
Capacity
Demand
On Time Delivery
FIFO
Rotate Stock
Quality
Cost
Supply
• Requirements
- Communications
- Specifications
- Expectations
- Timing
GROCERIES
J.I.T
Notes: Lets talk about pull. Pull systems are similar to other systems like “just in time” (jit), material as needed (man), and kanban.
Pull got its start in America in the grocery business:
The grocer replaced on their shelves, products demanded or “consumed” by the customer.
The grocer needed deliveries on time, the proper brand, and the right price and size to satisfy the customer.
To do this, the grocer used jit, communication with both supplier and customer, and rotation of stock F.I.F.O.
Walk through transparency as customer consumes, determines need, obtains from grocery store, who identifies needed replacement to supplier who delivers as need is identified.

## Slide 7: Synchronous / Lean Manufacturing Pull System
75¢
m
m
m
m
m
m&m
m&m
m&m
m&m
m&m
m&m
m&m
m
E M P T Y
mmmn
mmmn
mmmn
mmmn
mmmn
mmmn
mmmn
mmmn
Provider
Consumer
Replaces
Used
Products
Uses
Products
m&m
Notes: Pull system is a visual replenishment of goods just like a vending machine, where the provider replaces only what the consumer uses.

## Slide 8: Replace Consumption
1/4
1/2
3/4
F
E
Fuel Tank
Point of
Replenishment
Notes: We use pull signals in everyday life. An example is a gas gage. Without the signal we would have to anticipate our usage of fuel. Thus, running out of gas of filling the tank too often, wasting time. Just like the pull system the gas gage usually has a red zone also.
Ask for other examples of everyday pull system like: most groceries, batteries, etc..

## Slide 9: Push vs. Pull
Make all we can
just in case.
Make what’s needed
when we need it
Production Approximation
Anticipated Usage's
Large Lots
High Inventories
Waste
Management by Firefighting
Poor Communication
Production Precision
Actual Consumption
Small Lots
Low Inventories
Waste Reduction
Management by Sight
Better Communication
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
PARTS
Notes: Discuss with group the comparison of push and pull:
Push:
Make all you can just in case you run out of material. Just in case the machine goes down, just in case you run into a quality problem.
Pull:
Make only what the customer needs when they need it.
Push:
Approximate production based on what the customer anticipates they will need.
Pull:
More precise production based on what the customer has actually consumed. Customer and supplier agree upon a buffer size they would like to keep between them. As the customer pulls apart from the buffer, the supplier is authorized to put that quantity of parts back into the system.
Push:
Large lots lead to high inventories which hide problems and cause quality problems to increase because bad parts are found later and there are more of them.
Pull:
Smaller lots lower inventory level and drive problem resolution. Quality problems are contained with less parts to sort.
Push:
Waste time and resources running parts that are not necessary. May be more effective for the long term to shut down the machine and do planned maintenance or send an operator to training, solve quality problems.
Pull:
Reduces waste and provides time to do things we typically do not make time to do..preventative maintenance, housekeeping, training, problem solving, team meetings.
Push:
Always in firefighting mode trying to determine what is hot, how much inventory is there.
Pull:
System is controlled by visual management. Communication improved by gradual feedback the supplier receives from the customer in the form of a pull signal rather than finding out as the customer runs or is running out of parts, leaving little or no time to react. Customer and supplier communication is improved just by getting them together to set up a pull system.

## Slide 10
A Pull System Is Flexible and Simple
Objectives:
  Methods of controlling and balancing the flow
  Of resources.
  Eliminating waste of handling, storage, expediting,
  Obsolescence, repair, rework, facilities, equipment,
  Excess inventory (work-in-process & finished).
  Manufacture and ship only what has been
  Consumed.
  Provides visual control of all resources.
Notes: Read slide. Discuss what pull system objectives are.
It’s simple to use, but not so simple to design and implement. It’s a system that can be used for all kinds of processes and resources - not just material.
What a pull system is not!
Complicated and sophisticated
Only for a manufacturing process

## Slide 11: Pull Signals
NUMBER
QUANTITY
WIDGET
ADDRESS
1
2
3
4
5
6
7
8
9
Electronic
Signals
Instruction Sent From the Consumer to the Provider to Replace Resources that have been Used
Computer
Signals
Cards
EMPTY
Container
Exchange
Notes: Pull signals can take a variety of forms. Customize the signal to the process.
The major types of pull signals are shown on the transparency:
Cards
Containers
Computer signals
Electronic signals (andon boards)
Some others are:
Chips
Fax
Colored floor space
Let’s investigate card pull signals.

## Slide 12: Example of an “Internal” Pull Signal Visual Control Board
Information
Notes: This is an example of a pull board that could be used with internal operations, as shown, or even with external customers. The board in broken into three color bands:
Red zone indicates the supplier is on the verge of not satisfying their customer. Very low level of goods maintained.
Yellow zone indicates customer requirements are being met. Low level of finished goods maintained.
Green zone indicates the customer’s needs are being fulfilled. Supplier is building more than the customer is requiring and it may be time to stop production until demand is more in line with supply.
The cards hanging on the hooks in the colored zones reflect the part number identified in the section, a given quantity of material in one container. When a card is on the hook it indicates an empty container. When the hook is empty, the card has been placed on the container and it is full of material.
Other pertinent information (e.g.. Quality performance) would be contained in the information section.
The next transparency displays the process flow.

## Slide 13: Pull Signal - Card
Point of
Manufacturing
Point of
Use
Standard
Pack
Container
Standard
Pack
Quantity
Description
Part Number
Designated
Storage
Area
STORE
MN
10/12/98
Notes: This is an example of how a pull card might be designed. Each organization should develop one that meets their particular situation. The example does display key information that should be shown to support the process.

## Slide 14: Reverse side of Pull Signal Card
If found,
return to
MA, or ship.
area
Thank You
10/12/98
Notes: One of the great fears with the use of cards is the possibility of cards being lost, stolen, or mishandled. Much of this is exaggerated, but can be minimized with information on what to do with a found card and overall training of the purpose of the cards within the organization.

## Slide 15: Pull - Loop Flow Diagram
Pull Signal
Material with Pull Signal
Visual Control
Board
Weld Test
Assembly
Pipe
Shop
4
3
1
2,5
6
10/12/98
Notes: Review this pictorial of a pull loop process flow.
The process would involve (1) an operator filling a container with material, (2) placing a card from the board on the container, (3) the container being shipped to the supplier, the supplier emptying the container, (4) the supplier returning the container, (5) the operator removing the card from the empty container and placing on the next available hook going from the bottom hooks to the top hooks, (6) the container place at the station for filling.

## Slide 16
De-Coupled Pull Process
8:00 Card / delivery person walks by, picking
up cards while delivering material
8:05 Operator puts out card “A”
9:00 Card delivery person walks by, gets
Card “A”
10:00 Card “A” material is filled by supermarket
Person
11:00 Card “A” material is delivered to the
Operator
Need Minimum 3 Hours of Material
At the Operator
10/12/98
Notes: When looked at in this manner you see the minimal interaction required between parts. The system takes care of all the indicators/signals required.

## Slide 17
My parts
are hot!!
My parts
are hot!!
??
??
Customer A
Customer B
Supplier
Is This Familiar?
10/12/98
Notes: This transparency can be used to describe one of the benefits in having a pull system with a visual control board.
Originally the operator / or supplier was constantly be told by his/her customers (internal or external) that their respective parts were hot and needed to be run. This caused a lot of confusion for the supplier, excessive changeovers, and a lot of effort on the part of the customers to keep track of material availability.
After implementation of the pull system with visual control board the operator / supplier would schedule part production based on the information provided by the control board. This reduced changeovers, eliminated confusion as status could be seen at a glance and situations developing noted, and reduced the need for customers to monitor/schedule materials.

## Slide 18: Pull Signals
NUMBER
QUANTITY
WIDGET
ADDRESS
Electronic
Signals
Instruction Sent From the Consumer to the Provider to Replace Resources that have been Used
Computer
Signals
Cards
EMPTY
Container
Exchange
1
2
3
4
5
6
7
8
9
10/12/98
Notes: Returning again to the types of pull signals, lets investigate container or dolly exchange.

## Slide 19
Pull Signals
CONTAINER OR DOLLY EXCHANGE
Uses the empty container as a physical signal that authorizes
The replenishment of the consumed material.
Requires space for two containers
Operator must draw from one container
At a time
Bulky material
EMPTY
10/12/98
Notes: Read and discuss this type of pull signal.

## Slide 20: Why a Standard Pack?
Specific number of parts = 1 Container of parts
1 Standard pack = 1 Pull signal
1 Container of parts = 1 Standard pack
Supplier
Toy Co..
Part
Number
Toy Strut
Customer
K2 Dock
Lot
Size
Seq.. No.
=
Pull Signals
CONTAINER OR DOLLY EXCHANGE
10/12/98
Notes: Read transparency and stress that one pull signal is equal to one standard pack which contains a specific number of parts and which correlates to container size and ergonomic weight/dimensions.

## Slide 21: Pull Signals
NUMBER
QUANTITY
WIDGET
ADDRESS
Electronic
Signals
Instruction Sent From the Consumer to the Provider to Replace Resources that have been Used
Computer
Signals
Cards
EMPTY
Container
Exchange
1
2
3
4
5
6
7
8
9
10/12/98
Notes: Again the types of pull signals, lets now look at electronic signals such as a material light board.

## Slide 22
Pull Signals
MATERIAL LIGHT BOARD
Uses lights to signal the need for bulk material replenishment
At a pre-determined re-order point.
Operator sensitive
Re-order point calculation is critical
Large, non-hand carriable containers
Container is fork lift compatible
Use as last-resort solution
PART #
1234567
PART #
1234567
PART #
1234567
PART #
1234567
PART #
1234567
PART #
1234567
10/12/98
Notes: Read and discuss this type of pull signal.

## Slide 23
Material Order Indicator
Material
Staging
Container
Removal
Material Order Point
Pull Sign
Pull Signals
MATERIAL LIGHT BOARD
10/12/98
Notes: This is a pictorial of a pull signal system using electronic signals to communicate.
Remember, we want to compress value-added areas, reducing lead time which will increase throughput and reduce cost.
Here we have three types of material that is located in a material staging area, away from the assembly point. At the assembly point we have only enough material on hand to meet needs for a short period of time (e.g.. Two hours) - may be two containers. When the operator empties one container a signal is turned on to signify needed replacement which shows up on the board identifying the part number. The material truck driver notes the signal, picks up the right material, delivers to the assembly area, picks up the empty container, puts in container storage and goes after the next signal.
The process involves minimum intervention and schedules based on need.

## Slide 24: Pull Signals
NUMBER
QUANTITY
WIDGET
ADDRESS
Electronic
Signals
Instruction Sent From the Consumer to the Provider to Replace Resources that have been Used
Computer
Signals
Cards
EMPTY
Container
Exchange
1
2
3
4
5
6
7
8
9
10/12/98
Notes: The last signal in our sample is the computer signal. Many are familiar with this method, using computer printouts or fax’s to indicate need for replacement. This can be operated much like cards, except the signal does not involve a board and does not involve cards. This method is used a lot when distances are great and both simplifies and speeds up the communication.

## Slide 25
Guidelines for Types of Pull Signals
10/12/98
Notes: This can be used as a guideline for determining the type of pull signal to be used based on the conditions that exist with the customer and supplier.
Discuss as is necessary.

## Slide 26
Loop 1
Loop 2
Loop 3
Loop 4
10/12/98
Assembly
Operation 20
Operation 10
Raw Material
Finished Goods
Notes: Place transparency on overhead and ask group for examples of where pull loops may be appropriate for their area.
A pull loop is usually required between two operations if it has been necessary to hold float between them in the past. A typical scenario is one in which two operations run at different rates. Refer to the flow diagram on the transparency. When operations 10 and 20 become synchronous (i.e.. Run the same model, at the same rate, simultaneously with no float in between) loop 3 could control the flow from operation 10 to assembly and loop 2 could be eliminated.

## Slide 27
Internal Loop Planning
Pull System Coordinator
Plant/area pull coordinator
Supplier
Operator
Supervisor
Process Engineer
Customer
Operator
Supervisor
Material Handling
10/12/98
Notes: When establishing a pull system loop it is essential the supplier and customer meet to define, agree, and understand all the aspects of how the loop will be implemented.

## Slide 28
How Many Pull Signals?
What should be considered in establishing maximum inventory levels?
Long changeover times
Long lead times
Machine downtime
Schedule increases / decreases
Large process or transfer batch sizes
Poor quality
Long cycle times
Bottleneck operations
10/12/98
Notes: In establishing the pull signals, we need to consider various key elements...Read slide.

## Slide 29: Pull Signal Monitoring — Case 1
Interpretation:
Customer requirements are being met.
Low level of finished goods is maintained.
Small lot sizes are produced on a regular basis.
Ability to changeover is not a problem.
Opportunity exists to remove signals from the loop.
Max Signals in Loop
Red Zone
Yellow Zone
Green Zone
# Signals
On Board
1 2 3 4 5 6 7 8 9 10 11 12 13 14
Days
10/12/98
Notes: It is best to establish a method by which to monitor the pull card movement, level of inventory so as to initiate corrective actions as is necessary. The pull signal monitoring chart supports this and is designed much like a visual control board regarding a red, yellow, and green zone. The total number of signals in the loop are displayed vertically on the left, and the time line showing the number of days that are monitored on the bottom.
Read interpretation.
“It may be desirable to build to the maximum inventory level in order to make time to work on continuous improvement (i.e.. Preventative maintenance, housekeeping, training, team meetings, quality, etc.)”.

## Slide 30: Pull Signal Monitoring — Case 2
Interpretation:
Department runs on the verge of not satisfying customer requirements.
Low level of finished goods is maintained.
Problems may exist that prevent department from getting out of the
danger zone (e.g., quality, downtime, changeovers.)
By not running into the yellow and green zones, the department is
unable to maintain the desired amount of safety stock.
Max Signals in Loop
Red Zone
Yellow Zone
Green Zone
# Signals
On Board
1 2 3 4 5 6 7 8 9 10 11 12 13 14
Days
10/12/98
Notes: Read transparency interpretation.
“If the supplier is not meeting the customers’ needs by dropping below the minimum inventory level that is agreed upon (running in the red), extra steps must be taken to correct the situation, running to the maximum inventory level (i.e.. The green zone)”.
“If the customer is not complaining, this may be a situation where the minimum inventory level has been set unnecessarily high initially to make both the customer and the supplier comfortable with the system. It is recommended that a pull loop be established starting out where you are today in terms of float in order to evaluate current conditions. The customer satisfaction charts will tell you if you have float levels too low or too high, and if your red zone needs adjustment (i.e.. Minimum inventory level)”.

## Slide 31: Pull Signal Monitoring — Case 3
Interpretation:
Customer requirements are being met.
High level of finished goods is maintained.
Department is producing more pull signals than required by customer.
Changeovers are not a problem; machinery may be dedicated.
Too many signals in the loop.
Max Signals in Loop
Red Zone
Yellow Zone
Green Zone
# Signals
On Board
1 2 3 4 5 6 7 8 9 10 11 12 13 14
Days
10/12/98
Notes: Read transparency interpretation.
“It may be desirable to stay at this level temporarily to resolve some problems before removing signals from the loop”.

## Slide 32: Pull Signal Monitoring — Case 4
Interpretation:
Large batch sizes are run.
Changeovers are infrequent.
Customer may not return pull signals on a frequent basis.
Process problems may prevent department from running smoothly.
Max Signals in Loop
Red Zone
Yellow Zone
Green Zone
# Signals
On Board
1 2 3 4 5 6 7 8 9 10 11 12 13 14
Days
10/12/98
Notes: This is an example of a system out of control. Investigation is required to determine why there is so much variation.
Read transparency interpretation.
“A spike in a chart could also indicate that signals have lost and somehow made their way back into the system all at once”.
“If the customer is not able to avoid batch running an operation, it may be necessary to move the point at which the signal is returned. The signal could be returned after the next operation that runs one day’s worth of parts, each day. This could be done in order to smooth out the flow of signals back to the supplier so that a situation where one day they are in the green and the next day they are in the red does not occur. It is important that the red zone does in fact indicate urgency. If a customer batch runs parts once per week and all the signals come back putting the supplier in the red, yet the supplier knows that the customer does not need those parts again until next week, the board is not being used properly”.

## Slide 33
How Will Pull System Change
Your Job?
Preventative maintenance
Quality improvements
Team meetings
Housekeeping
Training
Continuous improvement
Pull system provides more time for constructive activities
that will make your job and working conditions better
tomorrow because with pull you run only the parts that
are needed. Shut down time can be spent on:
10/12/98
Notes: All of this information, new approaches, reflect a lot of different ways to perform our businesses. However, change is concerning....You might ask, what would a pull system do to my job?
Read slide and discuss.

## Slide 34
Implementation of a Pull System
Is Affected by Many Factors
The process itself
Economics
Cost and availability of transportation
Relationship and logistics of supplier
Level scheduling
Containerization
Supplier, customer, and warehouse
Floor space
These are the reasons why there are only guidelines and not concrete rules governing the implementation of pull systems. Real data and common sense must be applied.
10/12/98
Notes: Implementing a successful pull system doesn’t just happen. It depends on proper preparation, understanding and involvement by all affected parties, and continued review to ensure it is operating properly and leading to improvements.

## Slide 35
Benefits of Pull Systems
Increases employee involvement
Allows decision-making at appropriate levels
Allows manufacture of only what is needed by
the customer
Improves communications of customer needs
through visual controls
Provides a common system for moving material
through a plant
10/12/98
Notes: Benefits of a pull system are summarized in the next two slides.
Read each and discuss.

## Slide 36
Benefits of Pull Systems
Continued
Eliminates scheduling complexities
Reduces lead time and work in process inventory
Highlights quality issues quickly
Organizes the workplace
Leads to lower unit cost
Supports continuous improvements
Counts inventory by counting number of pull
signals
10/12/98
Notes: Continue reading and discussing.

## Slide 37
Standard Pack:
  1 standard pack = 1 container = 1 pull signal
  1 days production = ( )
  1 standard pack = 1 days production / 10
  ( ) = ( ) / 10
Maximum Inventory Level (Max):
  Weekly average = 8 weeks inventory / 8
  ( ) = ( ) / 8
  Days of inventory = weekly average / planned daily production
  ( ) = ( ) / ( )
  Safety stock *s.s.) = additional inventory that must be added due
  to current non-synchronized operations.
  MAX = (days of inventory) X (daily planned production) + (s.s.)
  ( ) = ( ) X ( ) + ( )
Minimum inventory level (MIN):
  (MIN) = batch size = red zone = replenishment
  (MIN) = ( )
Number of Pull Signals in a Loop (nps)*:
  (nps) = (MAX) / number of pieces in a standard pack
  ( )* = ( ) / ( )
Number of Pull Signals in a Red Zone (RZ)*:
  (RZ) = (MIN) / pieces in a standard pack
  ( )* = ( ) / ( )
Number of Pull Signals in a Yellow Zone (YZ)*:
  (YZ) = (nps) - (RZ) / 2
  ( )* = (( ) - ( )) / 2
Number of Pull Signals in a Green Zone (GZ)*:
  (GZ) = (nps) - (RZ) - (YZ)
  ( ) = ( ) - ( ) - ( )
Designated Storage (dss):
  (dss) = (nps) X (length) X (width) / number of containers high
  ( ) = ( ) X ( ) X ( ) / ( )
* Round up to the next highest number
/ Means divided by
X Means multiplied by
Pull Signal Calculations
10/12/98
Notes: This is a worksheet for determining the number of pull signals, storage quantity, red/yellow/green quantities, etc. Use as a reference. Remember it is important that the customer and supplier discuss together the determination and execution of the pull signal arrangement.

## Slide 38: Observation Worksheet: Pull System
Key Point
Observations
Pull Systems
(Replenishment based on
consumption)
Pull Signals
(Type used & why)
Inventory Levels
(Stock, WIP, banks)
Stock Dates
(FIFO vs. FISH)
Distance Traveled
(Part, WIP,conveyor lengths)
Small Lot Production
(Minimum material quantity
and flow)
Containerization
(Quality part presented to
operator)
Supplier Involvement
(External of process or
obvious boundary)
Leveling
(Smooth flow vs. too much / little
work, equipment, facilities, people)
Notes: This is a worksheet for evaluating pull status and opportunities in the target worksite, use the key points as thoughstarters.