## Slide 1
-6
-4
-2
0
2
4
6
Quality Function Deployment (QFD)
- Developing Products/Processes Faster, Better, Cheaper!
Sigma Quality Management

## Slide 2: Agenda
Why Quality Function Deployment?
QFD in Product & Process Design
Building the First House of Quality
  Room 1 – Voice of Customer to Customer Requirements (CRs)
  Room 2 – Prioritizing Customer Requirements, Perceptual Mapping
  Room 3 – Defining Product/Process Requirements (PRs)
  Room 4 – Mapping PRs to CRs
  Room 5 – Technical Benchmarking
  Room 6 – Targets & Limits
  Room 7 – Conflicts and Synergies
“Living in the House” and CTQs
The Next Few Houses
Prediction, Verification & Validation

## Slide 3: Why QFD?

## Slide 4: Some Notable Product Failures
Product Failure | What Went Wrong
New Coke (1985) | Focused on taste tests while ignoring emotional attachment to the original product
Ford Edsel | Engineers emphasized technical features instead of what buyers wanted
Segway | Technology-driven product without sufficient customer need
Microsoft Zune | Copied iPod features but missed ecosystem, simplicity, and brand experience
Google Glass | Excellent technology but poor social acceptance and privacy concerns
Amazon Fire Phone | Focused on 3D interface instead of app ecosystem and battery life

## Slide 5: Why Quality Function Deployment?
Product Design
  Brings in the Customer as Key Performance Requirement
  Helps Identify Current Product Strengths & Weaknesses
  Early Identification of Design Conflicts
  Helps Drive Customer Requirements into Design
  Links to Later Verification & Validation Activities
  Reduction in Design Cost and Cycle Time (Rework Prevention)
Process Design
  Above, Plus . . .
  Process Design Often Occurs in a Vacuum – No or Limited Customer Input

## Slide 6: Some Notable Product Failures
Product Failure | What Went Wrong | How QFD Could Have Helped
New Coke (1985) | Focused on taste tests while ignoring emotional attachment to the original product | VOC would have identified "brand loyalty" as a critical customer requirement
Ford Edsel | Engineers emphasized technical features instead of what buyers wanted | QFD would have exposed mismatch between customer priorities and engineering priorities
Segway | Technology-driven product without sufficient customer need | QFD would have shown weak relationships between technology and important customer requirements
Microsoft Zune | Copied iPod features but missed ecosystem, simplicity, and brand experience | Competitive benchmarking in QFD would have highlighted gaps
Google Glass | Excellent technology but poor social acceptance and privacy concerns | VOC studies would have revealed appearance and privacy as critical requirements
Amazon Fire Phone | Focused on 3D interface instead of app ecosystem and battery life | Importance ratings would have shifted engineering effort

## Slide 7: QFD IN PRODUCT AND PROCESS DESIGN

## Slide 8: The DMEDV Development Process
Design For Six Sigma
Define
Measure
Explore
Design
Verify
Understand Customer Needs And Specify CTQs
Initiate, Scope, And Plan The Project
Develop Design Concepts And High-Level Design
Develop Detailed Design And Associated Processes
Test Design And Implement Full-Scale Processes

## Slide 9: Defining Product & Process Requirements
Phase 1 - Define
Phase 2 – Measure
Key
Deliverables
Project Charter/Multi-Generational Plan
Project Plan
Design Control Processes
Project Team
Market Concept
Product
Selection
“Best” Market
Concept
Product Idea “Pool”
Business
Vision/
Strategy
Technology
Concepts
Market
Insight
Customer Insight
Project
Charter
Vision
Prod.
Plat.
Multi-Generation Plan
Idea
Feas.
Devel.
Comm.
Launch
Review
Project Milestones
Detailed Customer
Input Collection
Observations
Interviews
Business, Regulatory
Manufacturing
Requirements
CTQ
Design
Scorecard
Competitive Performance
Benchmarking
Voice of the Customer (Qualitative)
Voice of the Customer (Quantitative)
Competitive Benchmarks
Customer Requirements
Performance Level Requirements/ CTQs
CTQ Scorecard
Deciding what to buy
Purchase process
After Initial Consumption
Before Consumption
Initial Consumption
Product receipt
Initial use
Becoming proficient if appropriate
Obtaining help
Solving problems
Maintenance
Disposal
Attractive
Indifference
Must-be
One-Dimensional
Requirements
Workbook
Gather VOC Baseline; Define
Customer Segments
Gather VOC Inputs
Analyze Data; Define Customer & Performance-Level Requirements
Assess Importance/ Satisfaction
Specify CTQs
Confirm CTQ’s
Impact
Probability
5
3
1
15
9
3
25
15
5
Define & Scope Project; Form Skeleton Team
G1
HOQ-1
Pre-DMEDVI

## Slide 10: Driving Requirements Into Product Design
Phase 4 - Design
Phase 3 – Explore
Phase 5 - Verify & Validate
Key
Deliverables
Producible Product Design (Frozen)
Component Design & Specifications
Optimized Production Process
Control Plans
Qualification Plans
Product Design Verified
Final Product Validated
Product Release Authorization (PRA)
Process Validated
Launch Quantities Produced and Shipped
HOQ-2
HOQ-4
Parts Requirements
Extrude/
Anneal
Cut
Assy
Process “X’s”
Supplier A
Process
Scorecard
Mix
Base
Pad
Seal
Capital
AR
Production Equipment
Fabrication
Process
Pilots
Optimization
Evaluation
Production
Design
Product, Packaging
Process Validation (IQ, OQ, PQ) Planning
Design (Product) Verification
Base
Pad
Seal
Process Control Plan
Develop Production Controls
Installation (IQ),Operational (OQ) Qualification
Performance Qualification (PQ)
OK?
Produce Launch Quantities
Ship Product
Process Design of
Experiments
Product & Process Measurement
Process Optimization
Vertical Startup
Plan
Detailed Product Design
“Feasible” Product Concept Design
Preliminary Process Design
Feasibility Assessment
Concept
Evaluation
Design Concept
Generation
“Best” Product
Design Concept
HOQ-2
HOQ-2
Product Requirements
Subsystem Requirements
Transfer Function Y = f(X)
Cut
Assy
Package
Design for “X”
Extrude
Preliminary Process Design
Concept Feasibility/Optimization
Benefits
Cost
Safety
Proof of Principle (Early Clinicals)
Preliminary Cost Analysis (COGS)
Concept Hazard Analysis
Initial Stability Study
$
Market
Market Plan/Claims, Prod. Brief
Manufacture
Assembly
Human Factors
Environment
Cost
Prototype Product
Design of Experiments
Support & Operational Readiness Plans
Detailed Process Design
Parts/Assembly Design
Parts Requirements
Prototype/Customer Usability Test
CTQ
Design
Scorecard
Requirements
Workbook
Verification Testing
Force
Transmission
Hole
Forming
Handle/
Force Applier
TDR1
G4
G3
G2
TDR2
TDR3
CTQ
Design
Scorecard
HOQ-3
Subsystem Requirements

## Slide 11: BUILDING THE FIRST HOUSE OF QUALITY

## Slide 12: “Good” Requirements
Requirements Analysis should generate:
Functions: What the system must do for the customer,
Performance: How well the functions must be performed,
Interfaces: Environment in which the system will perform, and
Other business & regulatory requirements and constraints.

## Slide 13: QFD Deliverables
Device shall cut tissue of 5 mm thickness at a rate of 1 cm/second
Surgeon transects tissue in minimal time
Customer Level Requirement
Performance Level Requirement
Is this a CTQ?
Critical to Quality (CTQ)
“Translated” From VOC

## Slide 14: Performance Requirement Components
The reason the requirement is included & justification for metrics
How we will demonstrate via objective evidence that the product meets the requirement
Clear description of the need represented by the requirement
*
* - for Customer Requirements, a Validation Strategy

## Slide 15: Exercise: “Good” & “Bad” Requirements
Objective | Distinguish between well-written and poorly-written requirements
Instructions | Review the Requirement Statements on the next slide Discuss whether the Statement is a “Good” Requirement. If not, how could you convert it into a “Good” Requirement?
Time | 10 minutes

## Slide 16: Requirements Exercise
Initial Requirement Statement | Good/ Bad? | Re-Written Statement
The device end-effector must be able to articulate through a range of +/- 30 degrees |  | 
The battery must last a really long time |  | 
After fitting, the concrete anchor must be secure as measured by a minimum pull-out force of 500 lbf |  | 
The axle bearing must be secured to the locomotive axle with a tight shrink-fit |  | 
The entire maintenance procedure should take no more than 2 hours. |  | 
Hint: Does the Requirement Statement include a Function & Metric/Target?

## Slide 17: House Of Quality: Core QFD Deliverable
What are the Rooms and what do they do for you?
What Question does each Room ask?
What are the Relationships of the Rooms in the House?
Where are the CTQs?
1
Customer
Requirements
(V)
3
Performance Requirements (I)
Target Goals
7
Correlation (I)
2
Customer
Rating
(B) (V)
4
Relationships
(What vs. How)
(I)
6
5
Importance (V)
How Important
Targets/Specs(B)(I)
Technical Evaluation (B)
(V) = Comes from VOC information
(B) = Comes from Benchmarking information
(I) = Comes from Internal expertise
Notes: What’s In It?
Detailed Customer needs
Customer ranking of requirements and how they rate the performance of suppliers
The result of translating the Customer requirements to measures (quantifying)
Relationship of identified measures to Customer requirements
Comparison against competitors
What performance is required to meet or exceed Customer requirements
The correlation between the measures
Where does this information come from?
Voice of the Customer
Benchmarking Voice of the Customer
Internal Expertise
Internal Expertise
Benchmarking
Benchmarking
Internal Expertise
Internal Expertise
Room
1 Customer Needs
2 Customer Rating
3 Characteristics/Measures
4 Relationships
5 Technical Evaluation
6 Targets/Specifications
7 Correlation

## Slide 18: A VoC to Requirements Process
Measure Phase Voice of Customer to Requirements
Gather VOC Inputs
Identify Gaps and develop Market Research Plan
Plan customer interviews and observations
Develop Customer Requirements & Validation Strategy
Translate VOC & Characterize Requirements
Develop Performance Requirements & Link to Customer Requirements
Develop performance metrics, targets/limits and Verification Strategy
Confirm/ Validate requirements & determine weighting & value
Analyze survey results -prioritize Customer and Performance Requirements - determine CTQs
Gain baseline understanding of opportunity (mission)
Understand customer segments (Customer Matrix)
Gather competitive benchmark data
Gather reactive voice of the customer data
Gather VOC Baseline
Pre-DMEDVI & Define Phase
3. Gather qualitative customer data
Notes: Changes to Process
  Do concept testing after you understand the Customer Requirements
  Use of Field Visits to supplement the data needed to develop requirements
  Use language in Customer Requirements that are solution free
  Confirm Requirements and prioritization with customer

## Slide 19: QFD Example – Project “Crab Claw”
We’ll use an example of a device being designed to secure a stack of papers together. Our company has a current “pin” product on the market and there are several competitive “clip” products.
Our Product

## Slide 20: The House of Quality
Room 1

## Slide 21: Customer Needs: Room 1
1
Customer Requirements
Room 1 Objective:
Identify detailed Customer needs for product or service
Develop Customer Requirements
Input:
Process Understanding
User Environment(s)
Customers/Segmentation
Qualitative Voice of Customer
“Hierarchy” – general to detailed Customer Requirements
Also – Input from other customers (business partners, stakeholders)
Notes: Relationship Matrix
Strong
Moderate
Weak
Weight
9
3
1
Primary Need
Secondary Need
Tools used in VOC to organize information
Affinity Diagram
Structure Tree
  Needs must be personal, non-technical statements of Customer expectations
Room 1 Reminders
  Basic expectations and satisfiers must be provided in the design; delighters should be provided if possible
  Needs can be collected through surveys, interviews and observations
  Needs should be grouped into 2-4 levels using affinity diagrams/structure tree (20-30 groups max.)
  Get Customers involved in affinitizing needs when possible

## Slide 22: Process Observations
Team members observe process with customers and ask questions:
Look for unmet needs, frustrations, and challenges
Look for compensating behaviors
Understand the environmental factors that impact the job they are trying to achieve
Look for interactions between users, customers – i.e. “4P’s” or equivalent
4P’s – Problems, Preferences, Perceptions, Priorities

## Slide 23: Use Environments
Physical Location (Home, Office, Train, Plane, …)
  Type: Small vs. Large Office
  Lighting, ambient noise, temperature/humidity
  Motion and Vibration
Mental Workload of person
  Imposed by product plus environment
  Low vs. High Stress environment
Physical Workload – Stress on User
  Time to make decisions, trying to hold papers while applying current device
Presence of “Others”
  Product designed for Adults – how can presence of children affect use of product?

## Slide 24: Select Users/Customer Segments
Choose customers/segments based on
  Capabilities to serve existing customer needs profitably today, tomorrow, and the future
  Ability to serve potential/new customer needs
Involve customers who use competitors’ products and your products
Identify the stakeholders (all the people in the food chain)
  Purchasing, Stockroom, Users
  Government
  Regulatory agencies
  Internal departments
  Intermediary external customers/distributors

## Slide 25: User/Customer Segmentation
One Typology of Customer Segments:
Demographic | Behavior | Attitudinal | Aspirational
Easy to measure Easy for competitors to measure May not predict sales | Fairly easy to measure Highly predictive of sales | May predict sales Dynamic Can provide competitive advantage | Fantasy Reality
Not a source of competitive advantage Doesn’t help understand why | Fairly easy for competitors to measure | Difficult to measure | Difficult to measure
Advantages
Disadvantages

## Slide 26: What Do We Still Need to Know?
Identify research gaps using components or dimensions of Quality
Determine what you know (that you have data to support) and what you do not know
Determine type of customer information you still need
QUALITY
  COST
  DELIVERY
SERVICE/ SAFETY
CORPORATE RESPONSIBILITY
Focus on the benefits, functions/use provided by the service/process
Focus on how much the benefits cost the customer
Focus on the timeliness or quantity of the benefits
Focus on after sales service not injuring the customer
Focus on legal, regulatory, reimbursement or environmental needs

## Slide 27: Consider Entire Consumption Life-Cycle
Deciding what to buy
Purchase process
After Initial Consumption
Before Consumption
Initial Consumption
Product receipt
Initial use
Becoming proficient if appropriate
Obtaining help
Solving problems
Maintenance
Disposal
Be sure to learn about problems relating to the entire life cycle of ownership
Which of these areas are important for your product development project?

## Slide 28: Exercise: Case Study Research Gaps
Objective | Identify Current Knowledge Gaps; Plan Research to Close
Instructions | Choose a Case Study (Camp Seat, Helping App – see next slide) Identify What You Think You Already Know About the User’s Needs Generate a List of Questions/Issues You’d Like to Have Clarified Via the VOC Effort
Time | 20 minutes

## Slide 29: QFD Case Study Choices
Case 1 – You are a manufacturer of camping equipment. You have a current camp seat on the market but it’s not selling well. You want to develop the requirements for a new seat.
Case 2 – You have an idea for a new Smartphone app. The app will connect people who want to help with elderly or poor people who need help (food, clothing, temporary shelter, simple tasks). You want to develop the requirements for this “helping” app.

## Slide 30: What Types of User Input?
Objective: Empathize with the user/ Confirm activities (e.g. # papers pinned)
Means: On-site 1 on 1 interviews with the user
Quantitative
Market Research
Formal Qualitative
Market Research
Telephone Calls
Mail Surveys
Internet Surveys
In-depth Interviews
Focus Groups
Customer Panels
Customer Interviews
Observational Research
Office Tours
With the User in Their Environment
Objective: Objective, unbiased questioning by a trained moderator, providing video capture of info.
Means: Sponsor of research not disclosed. Recruited to a qualitative research facility.
Objective: Objective, unbiased questioning by a trained interviewer or self-administered
Means: Sponsor of research not disclosed. Good for quantifying qualitative findings.

## Slide 31: Generic Interview Guide
Ask for examples!!!
1. Introduction
2. Bonding and rapport (“sailfish on the wall”)
3. Describe your job or your role within the organization
4. Describe your typical day – likes and dislikes. Best day, and worst day. (As if I were a video camera on your shoulder.)
5. What about your job, or what you do, keeps you up at night?
6. Describe your ideal way of doing your job – or, if you had a magic wand, what would your job be like? (Describe the ideal “product” is an optional way of asking this.)
7. Describe a quality product and why you chose it as a quality product
8. What changes do you foresee in the future that will change how you do your job?

## Slide 32: Crohn's Disease Surgeon Discussion Guide
Introduction
Bonding and rapport
Describe the environment you work in. Describe your practice focusing on treating Crohn's Disease (# of patients with early stage CD? # of visits per patient? Typical age / sex / weight? Type of treatment?).
Describe your typical day relating to treating Crohn's Disease – likes and dislikes. Best day, and worst day. (As if I were a video camera on your shoulder.)
  Strictureplasty, Resection, Abscess Drainage, Fistual Repair? Early CD patients?
  If don’t use the above treatments, why not?
  Working relationship with assistant (Describe the value of working mostly alone or using a team approach?)
  Typical procedure time?
What bothers you most about your ability to treat Crohn's Disease or keeps you up at night?
  Using Strictureplastry? Resection?
  Complications during a CD treatment? Bowell wall movement during a procedure?
Describe your ideal way of treating Crohn's Disease – or, if you had a magic wand, what would it be like? (Ideal “procedure”)
  What to view during a procedure?
  What about Resection? What type of data (time / # patients / success rate)?
  Knowing you have completely resected the bowel (know you are complete)?
  Reproducible and consistent resection?
Describe the ideal instrument to treat CD and what problems it would solve (Describe the ideal “product”.).
  Indicator of confidence?
  Bowel resection closure?
  Displays? Lights? Brightness? Colors? Audible indicators? Error indicators? Background noise (warnings / pumps / RF tones)?
Describe a quality product and why you chose it as a quality product
  Features you like in equipment you currently use and why?
What changes do you foresee in the future that will change your therapies for Crohn's Disease?

## Slide 33: Exercise: Develop an Interview Guide
Objective | Develop an Interview Guide for the Case Study
Instructions | Review the Questions/Issues You Generated Previously Develop an Interview Guide to be Administered to the targeted Users
Time | 25 minutes

## Slide 34: Respect the Customer but Probe!
Skimming the Surface
Interrogation
(You are not a casual observer)
(You are not an investigative reporter)
Walk in your customers’ shoes:
How Many Paper Sheets?
User (during Interview) – “No More than 4 or 5”
Team (during observation) – 60!!!

## Slide 35: Exercise: Gathering Customer Needs
Objective | Practice Gathering Voice of Customer Through an Interview Technique
Instructions | Two Groups - Interviewers, Users (Pick One Segment) Interview the User Using the Interview Guide note: make this as “fruitful” as possible; you’ll use these results in later exercises – eventually determining the CTQs for your case study Change Roles; Give the Users a Chance to Practice Interviewing.
Time | 40 minutes

## Slide 36: Develop Customer Requirements (Solution Open)
Purpose: Clearly state the Customer Requirements implicit in the verbal data from the interviews
Major elements:
  Identify Functions (What) the User Performs and How Well (Performance) the Function needs Performing
  Develop Customer Requirements Statements using the translation guidelines
Benefit: Enables the imagination and creativity of the team to contribute to the development of Customer Requirements, prevents blindly translating customer inputs to Performance Requirements

## Slide 37: Customer Requirement Elements
Identify Verb Identify missing functionality by answering the question, “What functionality is desired but missing for the user?”
Identify Subject Who or what performs this functionality?
Identify Modifier What is scalable or variable about the functionality?
Subject + Verb + Modifier
I’ll Help You With This Part!!!

## Slide 38: Translation Process & Example
VOC/Rqmt. | Statements & Translation
Voices (from Users, Transcripts) | I need to cut the targeted tissue without harming adjacent tissue When I nicked that artery, it seemed like there was blood everywhere
Customer Requirement Statement | The surgeon (subject) positions (verb) scalpel (object) with maximum stability (modifier) Subject + Verb + Modifier, also Rationale & Validation Strategy
Gather Related Voice Statements
“Extract” Subject-Verb-Object-Modifier
Create Customer Requirement Statement

## Slide 39: Translation Guidelines
No statement of means
  Avoid solutions - state the requirement or functionality
Avoid abstract language
  Avoid words like “good, easily, comfortably, reliably, accurately” which mean different things to different people
  Must be actionable
Use multi-valued language
  Describe what is scaleable about the functionality
  Use language that implies a range of functionality

## Slide 40: Focusing the QFD
Include “NUDs” in Your House:
New Needs – features or performance your product has not historically delivered
Unique Needs – features or performance that are distinctive or highly desired beyond the numerous other less-demanding needs that must be provided
Difficult to fulfil needs – features or performance that is highly desired but is quite difficult for your business to develop and will require special efforts/investments or resources on your part.
Don’t Include the “Old, Common, Easy” Needs!

## Slide 41: Project “Crab Claw” – QFD Room 1

## Slide 42: Exercise: Develop Customer Requirements
Objective | Develop Customer Requirements (Room 1) for the Case Study
Instructions | Review the “Voices” you obtained from the practice interview (your notes are also a valid source here) Develop a set of Customer Requirements (Function-Modifier) for the Case Study Input these to Room 1 of the House of Quality
Time | 30 minutes
House of Quality Templates:
QFD-OneSheet
QFD Matrix
QFD-Large

## Slide 43: The House of Quality
Room 2

## Slide 44: Customer Rating: Room 2
2
Customer
Rating
Importance
Objectives:
Determine Customer Requirements importance rating
Define how your organization is perceived compared to the “best of the competition”
Inputs:
Quantitative Voice of Customer (needs prioritization)
Quantitative Customer Perception – Our existing product vs. Key Competitors
Notes: Determination of Importance of Customer Want and Need:
  Establish rating scale (1 to 5 scale is typical with 5 the highest). The high number in the scale should represent best-in-class.
  Consider frequency of response when assigning ratings.

## Slide 45: Self-Stated Importance/Satisfaction Surveys

## Slide 46: Importance/Satisfaction Survey
Asks How Important a Requirement Is To Customer Segment
“How Important To You is the Amount of Effort Required to Secure the Papers?”
Likert Scales (1 – 5, 1 – 7) Employed to Quantify Priorities:
  1 – Not At All Important
  2 – Somewhat Important
  3 – Important
  4 – Very Important
  5 – Extremely Important
Asks How Current Product Satisfies Customer Segment
“How Satisfied Are You With the Amount of Effort Required to Secure Papers with the current Model XYZ Device?*”
Likert Scales (1 – 5, 1 – 7) Employed to Quantify Priorities:
  1 – Not At All Satisfied
  2 – Somewhat Satisfied
  3 – Satisfied
  4 – Very Satisfied
  5 – Extremely Satisfied
* - Should Also Be Asked for Competitors’ Products

## Slide 47: Project “Crab Claw” – QFD Room 2
Room 1
Room 2

## Slide 48: Exercise: Develop Room 2
Objective | Develop Importance/Satisfaction Scores for Customer Requirement Statements
Instructions | Pretend you are the Customer/User Using a 1-5 Likert Scale, Rank the Importance of the Customer Requirement Statements Pick a “Competitor” for your Current Product. Using a 1-5 Likert Scale, Rank the Perception the Customer/User has for your current product and the competitor. Complete Room 2 of your House of Quality
Time | 30 minutes

## Slide 49: Customer Rating: Room 2
Tips:
The User should be the primary source for determining the importance of a need
Choice of competitors should be market leader or most distinguished organizations, your direct competitors
The User provides perceptions of competitors’ effectiveness in satisfying needs
The highest rating on the scale is typically reserved for how the “perfect service” performs

## Slide 50: The House of Quality
Rooms 3 & 4

## Slide 51: Performance Requirements: Room 3
Performance Requirements
3
Objectives
Translation from Customer Requirements to Performance Level Requirements.
Methods
Use your knowledge of the product/service to identify product functions & metrics
Use benchmarking information to list how products/processes are commonly measured in like and unlike industries.
Use VOC information by asking “How might you measure if this requirement was being met?”
Also list existing metrics currently in use for similar designs.
Notes: Don’t worry about having too many characteristics/measures. These will be scored in Room 4, and only the ones most important to the Customer will become requirements for the design.

## Slide 52: Performance Level Requirement Statements
Contains a clear description of the device’s function and associated metric,
Communicates the intent of the requirement clearly to all who read it, and
Creates a foundation for product design and verification.
Subject: “Device” vs. “User”
“Shall” vs. “Should” vs. “Will” – firm vs. goal or aspiration vs. fact

## Slide 53: Verbs Have Meaning!
Identify Verb Identify missing functionality by answering the question, “What functionality is desired but missing for the customer?”
Identify Subject what performs this functionality?
Identify Metric How will performance be measured, what target/limits?
Subject + Verb + Metric
Guv’mint Language (DOD, NRC):
“The Device Shall . . .” – firm requirement
“The Device Should . . .” – a goal or aspirational requirement
“The Device Will . . .” – a statement of fact
Notes: 53

## Slide 54: Translation Process – CR to PR
VOC/Rqmt. | Statements & Translation
Voices | I need to cut the targeted tissue without harming adjacent tissue When I nicked that artery, it seemed like there was blood everywhere
Customer Requirement | The surgeon (subject) positions (verb) scalpel (object) with maximum stability (modifier) Subject + Verb + Modifier, also Rationale & Validation Strategy
Performance Level Requirement | Scalpel control operation shall result in tip position movement of less than 2 mm from desired position. Plus Rationale & Verification Strategy
Review Customer Requirement Statement
“Separate” Device from CR (Function & Metric)
Create Performance Level Requirement Statement

## Slide 55: Performance Level Requirements: Room 3
Look for the “Subject-Verb-Object”
Notes: SuperSudzer Example: Characteristics and Measures: Room 3

## Slide 56: Performance Requirements: Room 3
Tips:
Achieving a Customer Requirement may involve several Product Requirements; one Product Requirement may achieve several Customer Requirements - don’t try to maintain a one-to-one CR to PR ratio
Some Customer Requirements may not have an obvious Performance Requirement; you may have to rely on a secondary or tertiary relationship to define an effective measure (i.e. hemostasis, “trackability”)
The question to answer is: How would we measure or evaluate that we satisfied this Customer Requirement?

## Slide 57: Relationships: Room 4
4
Relationships
(What vs. How)
“How”
Performance Requirement
“What”
Customer
Requirement
Objective:
Explore and map the relationship between our potential Performance Requirements and the Customer Requirements
Can this “how” (Performance Requirement) achieve this “what” (Customer Requirement)? And to which level?

## Slide 58: Relationships: Room 4
Relationship matrix
Strong
Moderate
Weak
Weight
9
3
1
Importance Score
Importance Score = Sum (priority score x relationship weight value)
4
Relationships
(What vs. How)
Priority
Rating
Method:
Using strong, moderate, weak, rate the relationship
Calculate a score for each cell by multiplying the priority rating for the Customer Requirement by the relationship weight value (9, 3, or 1) of each related cell
Add individual scores up to determine how important is the Performance Requirement
Conduct a reality check at the end to make sure order makes logical sense
Notes: Determining Significance Using The Matrix
  This is a vital step in the QFD process. The final analysis stage relies heavily on the use of the relationship symbols at the intersection of the wants and needs and characteristics/measures.
  Generally, the strong relationships are reserved for those cases in which the characteristics/measures are clearly a primary means to meet the related Customer want and need.
  The moderate and weak relationships are lesser relations as determined by the judgment of the cross-functional QFD team.

## Slide 59: Project “Crab Claw”: Relationships: Room 4
Notes: SuperSudzer Example: Relationships: Room 4

## Slide 60: Exercise: Develop Requirements
Objective | Translate Customer Requirements into Performance Requirements
Instructions | Select several Customer Requirements – convert it to a Performance Level Requirement Define an appropriate metric for each, develop a Rationale Statement & Verification Strategy Input these to Room 3 of your House of Quality.
Time | 45 minutes

## Slide 61: Requirement Rationale
Provides description of the reason each requirement is included and justification for associated requirement metrics.
Helps the requirement originator confirm that the requirement is necessary and properly stated.
Rationale documentation - critical to identifying assumptions and design intent (enables effective communication and change management throughout product life-cycle)
CR: User Maximizes Tree Size to be Grasped
PLR: Device jaw opening shall be greater than 30 inches
HOW?
Rationale: For the forests to be harvested, the maximum tree diameter is 24 inches

## Slide 62: Rationale - Points
Reason – why is requirement necessary?
Assumptions – understand and accept risk
Operational Concepts – expectations around device functions and/or customer use
Design Decisions – document tradeoffs, communicate design intent
Sources:

## Slide 63: Requirement Verification/Validation Strategy
V/V Strategy confirms the requirement can be validated (customer) and verified (design) later in development
Provides necessary details to apply the requirement to product design.
Establish your verification/validation strategy early in product development; eliminate confusion, delays
Note: the Traditional House of Quality does not include a “Room” for this – you can add this to your House or include it on a separate spreadsheet.

## Slide 64: Example – Validation & Verification Strategy
Customer Requirement: The operator wants to minimize time to cut sheet steel.
Validation strategy: Operator evaluation lab with Likert satisfaction rating of greater than or equal to 3.0 on 5-point scale; targeting sample size of 10 operators with minimum of 1 cutting operation in 8-gauge sheet steel prior to gathering ratings.
Performance Requirement: The blade system shall cut 8-gauge sheet steel with a minimum rate of 72 inches/minute.
Verification Strategy: Use 1 cutting device and 10 blades. For each sheet of steel, attach a new blade to the cutting device. Activate the generator in test mode so that calibration data is displayed. Energize the device at generator level 5 for 30 seconds so the blade tip is exposed and unloaded in air. Perform the cutting operation on a pre-marked pattern on the sheet steel. Record the cutting time in seconds.

## Slide 65: How Could These PLRs be Verified?
PLR: Device jaw opening shall be greater than 16 mm
PLR: Device force to fire staple row through 20 sheets of 90 lb paper shall be less than 25 lbf
PLR: Device shall cause staple to transition from “U” shape to “B-Form” with 99.9% Reliability

## Slide 66: The House of Quality
Rooms 5-7

## Slide 67: Technical Evaluation: Room 5
5
Technical Evaluation
Objective:
Develop the comparison of how your current product compares to its most serious competitors
Method:
Obtain competitor’s product data by benchmarking
Follow up on the benchmarking information to get additional information for the key Performance Requirements you have selected if needed
Strive to develop a competitive rating for every key Performance Requirement
Notes: Benchmarking your own and others’ products against the design measures which the team has established helps to define the level of real performance. It also helps you to answer the following questions:
  Has the team defined the right measures to predict Customer satisfaction?
  Does the product have perception, as opposed to technical problems?
Going back to benchmark additional measures is a relatively expensive and time-consuming process in most industries. Therefore, it is recommended practice to benchmark only against the critical design measures. Critical measures will typically be the ones with high importance scores. Special consideration may need to be given to a measure which is new or complex. Typically, a team might only benchmark 50% of the design measures.

## Slide 68: Example: Technical Evaluation: Room 5
Notes: SuperSudzer Example: Technical Evaluation: Room 5

## Slide 69: Technical Evaluation: Room 5
Tips:
If possible, anticipate Performance Requirements before beginning benchmarking
Good choices for competitors are market share leaders, competitors recognized in the industry, or product/ service providers with innovative technology

## Slide 70: CTQ Elements - Targets & Specifications: Room 6
How Important
6
Targets
Objective:
Develop preliminary targets and specifications for the measures that will deliver Customer satisfaction
Methods:
Identify the level of performance which the team believes is required to meet Customer requirements
Evaluate targets by asking:
  Will this satisfy the Customer?
  Will it make the company more competitive?
Specify allowable variation
  Where does a loss of function occur?
  At what point will the Customer not tolerate performance?
Specify “allowable” defect rates (Sigma targets)
Notes: How Should We Set Up Our Target Values?
  The final goal of many QFD projects is to set the Target Values for the design measures. This step occurs when the data gathered throughout the process is brought together and final decisions are made to answer the question, “What are we really going to do (with respect to this product or service)?”
  Setting Target Values should be relatively easy because:
    The team has already defined where they want their product to be positioned for the Customer.
    The team has benchmarked the existing products to gain a good understanding of what level of actual performance is required in order to produce the desired level of perceived performance.
    The team will soon evaluate the correlation between design measures in order to determine what compromises may be required and how those compromises will be made.
Taking into account all of this information, the team decides upon the targets which they will shoot for. Normally at this point, the team would not decide how they are going to achieve the target values. They are just stating, “We know that we have to achieve this level of performance if we are going to be perceived the way in which we want to be perceived.”

## Slide 71: Setting Targets/Specifications
Competition’s Performance
Target/ Specification
Customer Need
Drivers
Own Capability
Consideration
PR
Competition
CTQ
Notes: There is no cookbook for setting targets and specifications. This is a function of business know-how and technical expertise.
  Kano Model: Targets may be set after considering the type of need being addressed.
  Must-Be: The design must be based upon achievement of these requirements.
  More is Better: The better the performance, the higher the satisfaction. Doing better than the competition and/or understanding the relationship between the CTQ and Customer satisfaction are possible bases for targets.
  Delighter: There is little “downside” to not setting an aggressive target, but potential significant gain by being aggressive here.
  Tips: Current or projected capability to achieve a performance level should not be the primary basis for establishing targets. To ensure success in the market, the Customer and competitive information should be the primary drivers.

## Slide 72: Setting Specifications for Measures
Perceived
Customer
Value
Set the upper specification at 60 seconds where Customer satisfaction starts to fall off.
% Customers Satisfied
30 60 90 120 150 seconds
Notes: Other methods to set spec limits include:
  Competitors’ specs
  Benchmark data
  Legal requirements
Specifications should be set such that most Customers will be satisfied with the results.
Two-sided specs will usually have a different shaped curve.

## Slide 73: Performance Level Requirements – Targets
1
Customer
Requirements
(V)
3
Performance Requirements (How)(I)
Target Goals
7
Correlation (I)
2
Customer
Rating
(B) (V)
4
Relationships
(What vs. How)
(I)
6
5
Importance (V)
How Important
Targets/Specs(B)(I)
Technical Evaluation (B)
(V) = Comes from VOC information
(B) = Comes from Benchmarking information
(I) = Comes from Internal expertise
Principles for “Human” Targets:
Exert less than 30% of maximum strength
Maintain a “neutral arm position” as much as possible
Perform task without my expectations violated
Tool visually expresses methods of use
Minimize memory load on user
Clear and immediate feedback
Errors immediately identified & intuitively correctable
Consistent information – across tasks, systems
Provide shortcuts as experience is gained
Notes: What’s In It?
Detailed consumer needs
Consumer ranking of requirements and how they rate the performance of suppliers
The result of translating the consumer requirements to measures (quantifying)
Relationship of identified measures to consumer requirements
Comparison against competitors
What performance is required to meet or exceed consumer requirements
The correlation between the measures
Where does this information come from?
Voice of the Consumer
Benchmarking Voice of the Consumer
Internal Expertise
Internal Expertise
Benchmarking
Benchmarking
Internal Expertise
Internal Expertise
Room
1 Consumer Needs
2 Consumer Rating
3 Characteristics/Measures
4 Relationships
5 Technical Evaluation
6 Targets/Specifications
7 Correlation

## Slide 74: Allowable Defect Rates
LSL Target USL
“Bad Design”
“Sigma” targets should be set for CTQs - this is key to evaluating the design (see Design Scorecards, Later!)
LSL Target USL
“Good Design”

## Slide 75: Targets and Specifications: Room 6
Tips:
Consider Dr. Kano’s “Must-Be, One-Dimensional, Delighter” model when setting targets.
Don’t settle for just meeting the competitor’s performance
Consider your Multi-Generation Plan – what can you deliver today vs. tomorrow?

## Slide 76: Example: Targets and Specifications: Room 6
Notes: SuperSudzer Example: Targets and Specifications: Room 6
Note: Additional Rows can be added to include Spec Limits and Sigma Level Targets

## Slide 77: Correlation: Room 7 - The “Roof”
Target Goals
7
Correlation
Objective: Understand and establish the correlation between the characteristics and measures
Method:
Determine target goals orientation by asking the following questions:
If we increase this measurement, will that help to achieve the Performance Requirement?
If we reduce this measurement, will that help to achieve the Performance Requirement?
If we hit the target, will that help to achieve the Performance Requirement?
Notes:    It is recommended that the relationship matrix be filled by working in columns, considering the nature of the technical requirement and its orientation (For Maximize, Minimize, and Target).

## Slide 78: Correlation: Room 7: "The Roof"
Strong positive
Relationship
Positive
Negative
Strong negative
Objective:
Establish the relationship between the “hows” and its strength
Method:
Use four symbols to represent relationships:
  Positive relationships indicate synergy,
  Negative relationships indicate “conflicts”
Note: These Symbols are Consistent with those used by the QFD Capture Software Package; Other Apps May Vary
+
-
Notes: If Conflict Exists:
  Trade-off between measures may be required
  Use an alternate measure. (This may lead to a re-evaluation of Room 4.)

## Slide 79: Correlation: Room 7
Tips:
Negatively correlated Performance Requirements typically require a lot of time and forward thinking (innovation) in an attempt to satisfy both conflicting measures
TRIZ thinking can be an effective means of “busting” conflicts
Conflict resolution should focus on meeting the Customer needs, not the organization’s needs

## Slide 80: CTQ Correlations – Project “Crab Claw”
Do These Correlations Make Sense?

## Slide 81: Completing the House
Objective | Complete Rooms 5 – 7 of the House of Quality
Instructions | Room 5 – Identify some Competitive Products (same as used for Room 2). How do you think they stack up technically against your current product Room 6 – What targets and limits would you set for the Performance Requirements listed in Room 3? Room 7 – Based on these targets/limits, complete Room 7 – direction of improvement, synergies, conflicts?
Time | 30 minutes

## Slide 82: Project “Crab Claw” House of Quality
Notes: SuperSudzer House of Quality

## Slide 83: QFD Analysis – “Living In Your House!”

## Slide 84: QFD Approach to Developing CRs/PRs
2. Benchmarking
3. QFD
Internal
Experts
Outputs
  Determine & specify CR’s & PRs
  Select CTQs
  Understand potential PR synergies and conflicts
  Plan to manage CR/PR risks
  Revised Charter
  Updated MGPP
Voice of
Customer (VOC)
4. Synthesis
Business, Regulatory, Internal Partner Requirements

## Slide 85: Analyzing Your “House”
Pattern | Interpretation
Highest score on competitive comparison | Able to lead market with existing product
Low score on competitive comparison, but high score on technical evaluation | Market product’s technical advantages to improve Customer perception
Empty rows in Room 4 | Unaddressed Customer need – develop corresponding product requirement
Empty columns in Room 4 | Potential unnecessary product requirement – determine possibility of dropping requirement
Strong negative correlations in Room 7 | Many design trade-offs will be required; signaling need for “invention”
Diagonal pattern of strong correlations in Room 4 | One-to-one alignment of product requirements with Customer needs – no leverage of requirements
Low technical evaluation – Room 5 | Significant technical development challenge – just to catch current competitive products
Notes: QFD should not be done “mechanically.” The real value of QFD lies in the understanding of Customer needs and how the attributes of the new product/service relates to these needs.
Documenting the House of QFD helps ensure this understanding throughout the design project.

## Slide 86: Analyzing the House
Objective | “Live in Your House”
Instructions | What insights do you glean from reviewing the full House?
Time | 10 minutes

## Slide 87: Critical to quality Requirements (CTQ)

## Slide 88: CTQ Definition & Selection
Critical to Quality (CTQ) - A subset of critical Performance Level Requirements (PLR)s deemed to have significant importance to delivering the Value Proposition.
The requirement is measurable with targets and ranges.

## Slide 89
Determining if a Requirement is Critical or CTQ
Is Requirement a PLR?
Evaluate the Requirement against the following:
Important to delivering the Value Proposition?
Important to reducing safety risks?
Important to any key business drivers?
Technically difficult to achieve?
Any of the above apply?
Is critical requirement necessary to deliver the Value Prop?
Is the requirement (x) linked to at least one critical parent requirement (Y)?
Determine & verify which x’s have the most influence (~80%) on any linked critical parent requirements (Y’s)
Does transfer function show requirement is a Vital X for any parent requirement?
Requirement is critical
Requirement is critical and a CTQ
Requirement is critical
Requirement is not critical
Note: if critical requirement is subject to variation, track on scorecard
Yes
Yes
Yes
No
No
No
No
No
No
Yes
Yes
Start

## Slide 90: Perform CTQ Risk Analysis
Assess the impact of failing to meet the targets and specifications.
  What is the risk to the Customer?
  What is the risk to the business?
For significant risks, assess the likelihood of occurrence.
  Are the current competencies of the organization well matched to meet the specifications?
For significant risks which could occur, identify actions which could be taken to reduce or address the risks. What additional costs result from these actions?
If “Show-stoppers” exist, decide whether to proceed with the project.
Notes: Customer information should have given the team a sense for how important it is to the Customer for the design to meet the targeted performance. The team now needs to consider the risks of the design not being capable of consistently performing to the targets.
This phase usually ends with a project review by management. This is often the first time that management will have information which will allow them to compare the benefits of taking advantage of the opportunity with the costs of possible failure. If the risk is significant, the organization may decide to stop the project.

## Slide 91: Exercise: CTQ or Not CTQ?
Objective | Identify Requirements That Could be CTQs, Case Study CTQs
Instructions | Which of the following requirements could be a CTQ? Why? Force to Fire device shall be less than 45 lbs. Device shaft shall be 18 inches long Pump Seal leakage shall be less than 1 cc/min Component dimension shall be 25 mm +/- 0.2 mm Contact pressure (seal to hand) shall be less than 1.75 lb Develop what you think could be the CTQs for Your Case Study Determine Targets (e.g. a Target, Upper/Lower Limit, as appropriate) for the CTQs
Time | 20 minutes

## Slide 92: At A Meeting A While Back . .
“You Can’t Change a CTQ Without Marketing!”
Unhappy Marketing Lead

## Slide 93: Review Team Charter
Has the information gathered in this step:
  Affected the definitions of Generations 1, 2, or 3 of the new product or service?
  Affected the opportunity statement, business case, goal statement, or scope for Generation 1?
  Affected the team selection or sponsor?
  Affected the project plan?s
If yes, modify charter as appropriate and review with your sponsor
Notes: Often new information that is gathered during a project has implications for the team’s work in previous steps. The path for a project is usually not in a straight line from one step to the next. Instead, teams need to revisit previous thinking in light of what they have learned.
It is important to update the documentation as the team’s thinking unfolds so that the implications of the team’s growing understanding can be thoroughly thought through and the effects of changes are captured and communicated.

## Slide 94: THE NEXT FEW HOUSES

## Slide 95: Systems Engineering Process
For Complex Systems:
Allocate Requirements/Functions to Hardware, Software, Human “Systems”

## Slide 96: Cascade & Optimization – Flow-Down & Flow-Up
Translate to CTQ’s
Capture VOC
Translate to Process Req’mts
Translate to Comp. Req’mts
Translate to Design Req’mts
Analyze
Concept
Measurement System Definition & Analysis
Concept & System Engineering
Critical Parameter Management
Transfer Functions
Manufacturing Capabilities
Cascade
Design Optimization & Verification
Design Predictions
Notes: Focus on these differences that NPD teams will see in the outputs of each phase
(Those that you see are different
Or more emphasis are:
Critical Parameter Mgmt
Transfer Functions
Manufacturing Capabilities
Concept Engineering
Measurement System Analysis

## Slide 97: Design Relationships – a Model
Customer Rqmts
Performance Rqmts*
Performance Rqmts
Sub-System Rqmts
Sub-System Rqmts
Parts Rqmts
Parts Rqmts
Process Rqmts
* Performance Rqmts = Highest Level Requirements (i.e. Product)
House 1
House 2
House 3
House 4
Requirements May Also be Allocated Between Hardware and Software!

## Slide 98: “Simple” Cascade Example
“Performance Requirements to Subsystem Requirements”
Performance Requirement – Cutting Speed (in./sec.), Target – 5, LSL – 3
Subsystem Design:
Power
Supply (PS)
Motor
Driver (MD)
Rotating
Cutter (RC)
Voltage
Current
Frequency
Torque
Rotation Speed
Weight
Size
Torque
Speed
Cutter Size
Cutting Speed
Other Product Requirements
Pwr. Supply Motor Driver Rotating Cutter
Voltage
Current
Frequency
Torque
Size
Rotation Speed
Weight
Torque
Speed
Cutter Size
Strong or Direct
Medium or Indirect
Relationship:
House “2”
CTQ
Relationships are qualitative; Transfer Function describes quantitative…
Ex. Torque and Rotation Speed

## Slide 99: COMPONENT DEVELOPMENT ROADMAP
Start Component Design
Project Start
Component/Characterization & Qualification
Cut Steel
Component Qualified
Tool Qualification
Start Concept Tool Design
Inputs
Inputs
Inputs
Inputs
Inputs
CAR Estimates
Review Charter
COGS Estimates
Component Dev.
Roadmap into Project Schedule
Design
Material Selection
DFM / DFA
FEA Sim/ Part Fill Analysis
Design Frozen
NSR Dwgs DE’s Identified
Final Model / Database
Tolerance Stacks/
Budgeting
Tooling/ Process Development
Tooling/Capacity Plan
Refined RFQ Issue PO
TCOGS assess
Supplier Selection Finalization
Technology Select - final
CRR with:
TRR, -Gaging strat- Process Map-Equipment ER (if needed)
Gaging
Gage Concept Design /Review
Tooling Spare Parts
TFMEA
Tool Design Concept / Approval
Tooling
Process
Development
Tool Construction
Tooling
Tool Break-in
Tooling
Process Verification
Short Term Cap Study
Plant Component Documentation
I Sheets
Tool Metrology
Gaging
Gage Construction
Process Characterization & optimization
GR&R
Tool Capability Study
Preventative Maint. Plan
Gaging
Process Development
Long Term Capability Est
G10002 Submission & Approval
SR Drawing
Process Flow/Map Diagram
Control Plan
First Article
Stability Study
Tooling/Process Documentation
Tool /Process Doc. Package
Start PFMEA
Inputs
Supplier Assessments
VSIM/FEA Process Modeling Simulation
Define
Measure
Explore
Design
Verify & Validate
BOM
Refined Demand Forecast
CP0110 Sourcing Risk
Updated C/Matrix-Control Plan
Software Validation
Compatibility
Refined CTQ’s
Screening RFQ’s- w/early Delta’s
Initial DFM-Technology Select
Early Supplier Engagement
Initial CTQ’s
Initial Concepts
Initial BOM
Initial Demand Forecast
Predicted DP’s Identified
DP’s confirmed
Customs
Supplier Approval Letter
Stabilization/ LCM
Perf Metric monitoring
Lessons learned
Master Setup Doc’s
Prod.cap. = Demand +20%
Start Process Control Plans
Process Lean Evaluations
Start Packaging strategy
Packaging confirmed.
E-One Lot size confirmation
C/Matriix/ PFMEA/ Cplan linked
Revised CRR-as needed
Sub assy equipment (as needed)
Equip. Construction
Equip Safety review
Verify Model to Tooling
Prototype parts
Start Process Char. Matrix
E-1 Setup
Tooling continuity plans-Bridge
Stability Tasks
Tool Design documentation
Tool Capacity verification
Lean eval/lot sizing.
Component Design

## Slide 100: “Simple” Cascade Example
“Subsystem Requirements to Parts Characteristics”
Motor
Driver (MD)
Torque
Rotation Speed
Weight
Size
Torque
Rotation Speed
Other Reqmt’s (e.g. Weight)
Stator Windings
Rotor Windings
Wire Gauge
Shaft Diameter
Case Thickness
Shaft Length
Case Dimensions
Bearing Surface
Insulation Strength
Insulation Thickness
Strong or Direct
Medium or Indirect
Relationship:
Motor Driver Design
Others
Subsystem Requirements
Parts Characteristics
House “3”
Relationships are qualitative; Transfer Function describes quantitative to part characteristics
Critical
Critical

## Slide 101: ASSEMBLY PROCESS & EQUIPMENT DEVELOPMENT ROADMAP
Start Assembly Process Design
Project Start
Assembly Process Characterization
Equipment Design
Assembly Process Transfer
Equipment Build and Debug
Requirements Specification & Equipment Procurement
CAR Estimates
Product Inputs
COGS Estimates
Business Inputs
Design
Assembly Models/ Prototypes/ Drawings
NUDS Technology Assessment
Preliminary Line Balance
Assembly Equipment RFQ
Value Stream Analysis
Assembly Process Map
Preliminary DFMA
Tooling/ Process Development
Preliminary TCOGS
Preliminary Process Characterization Strategy & Costs
Production Components
End-to-End Process Characterizations
Measurement Systems Assessments
Equipment Processes Characterization
Define
Measure
Analyze
Design
Verify & Validate
BOM
CAR Estimates
Assembly RISDA
Preliminary PFMEA
Screening CTQ’s- Early Delta’s
Initial DFM-Technology Select
Early Supplier Engagement
Preliminary Product Requirements (PLRs)
Product Design Concepts
Prototype Components
Prototype Assembly Process
Product Demand
System Level Requirements (SLRs) and Customer facing Characteristics
Sub-System Reqmts. (SSRs); Critical Assy. Process Reqmts. (APR’s)
Technology Selection
Assembly Process Layout
Material Handling Concepts
Changeover Requirements
Human Machine Interface Requirements
Error Proofing Requirements
Machine Control Systems
Preliminary Selection Of Measurement Systems & Calibration Methods
Equipment Development Standards and Guidelines
Equipment Requirements Review
Supplier Selection
Preliminary Assembly Control Plan
Update Assembly RISDA
Update PFMEA
Infinity System Requirements
Preliminary CCPs identified
Selection of Measurement Systems and Calibration methods
Preliminary Safety and Ergo Review
Equipment Serviceability and Setup Review
MAKE site VOC input (VOF)
Release PO’s
Equipment Concept/ Preliminary Design approval
Equipment Fabrication Design approval
Equipment FMECA’s
Spare Parts Identified
Update Assembly RISDA
Update Process Development Schedule
Equipment Design updates
Production tooling Components
Equipment Debug
Equipment Dry Run
Spare Parts Purchase
Safety Ergo Approval
IM & TE requirements
Perform Equipment Calibration
Process Parameters Defined/Verified
Software Validations
Update PFMEA
Training at Supplier
Preventive Maintenance Plan
Validation (OQ & PQ)
MAKE Site Verification
Shipping & Customs Documents
Final Safety and Ergo
Training at MAKE Site
Equipment Shipment to MAKE Site
MAKE site Facilities Preparation
Equipment installation
Make Site Equipment Calibrations
Update
IM & TE requirements
Infinity System Hook-ups
Repeat Measurement Systems Assessments
Update Control Plan with identification of CCPs and Output Controls
Finalize Manufacturing Documentation
Complete Characterization Summary Report
Understand Transfer function for SLRs and Customer facing Characteristics
Confirmation run after installation
Equipment Documentation
Software issued
Installation Qualification
Confirmation of CCPs and Output Controls
Purchase fabricated spare Parts
Update Assembly RISDA
Tag Equipment
Make/Buy Decision
Process Design

## Slide 102: “Simple” Cascade Example
“Parts Requirements to Process Variables”
Process Design
Process Variables
Motor Driver Design
Turn Motor Shaft
Cast Case
Draw
Copper Wire
Wind Shaft
Coat Wire
Wind Stator
Assemble Bearings
Assemble Shaft/Case
Stator Windings (#)
Wire Gauge
Shaft Diameter
# Turns Applied SOP
Draw Die Diameter
Draw Die Speed
Lathe Setting
Coating Speed
Insulation Viscosity
Insulation Temp
Assembly Dimension
# Turns – Stator SOP
Others
Strong or Direct
Medium or Indirect
Relationship:
Others
House “4”
Supplier Process
Our Process
Again, relationships qualitative;
Transfer Functions provide quantitative.

## Slide 103: QFD Strategies
Customer Needs
Product Product CTQs
Needs Determined
Process
Needs Process CTQs
Determined
Consider the best QFD approach for your design project:
  Example: A team redesigning a contracting process organized customer needs by the product (e.g., the contract) and the process (negotiating the contract). Two QFDs were performed:

## Slide 104: QFD Pitfalls
QFD on everything rather than just high-risk areas
Too much chart focus and not enough analysis for new design
Ignoring CTQ conflicts
Not taking the time to do it right
Adherence to the “traditional approach”
Internal pressure causing loss of customer focus

## Slide 105: PREDICTION, VERIFICATION & VALIDATION

## Slide 106: Variation Prediction Philosophy
Design for Six Sigma encourages prediction of design’s ability to meet CTQ targets and specifications based on capabilities of manufacturing/ production processes
Design is iterated until targets and specifications are met at desired sigma (e.g., defect) levels
Design Process
Define Requirements
Develop Design
Develop More Details
Assess Capability
Not OK
(To Production)
OK
V&V

## Slide 107: CTQs – Managing Customer-Perceived Variability
-
1
.
0
-
0
.
5
0
.
0
0
.
5
1
.
0
1
.
5
Upper & Lower Limits – Customer Derived
Variation – Design & Production Controlled
CTQ

## Slide 108: Variation Prediction Purpose
CTQs’
(Y’s)
Product Design
What the Customer is Looking For (and Sees!)
What the Design
Team Identifies
& Develops
Process X’s
What
Manufacturing
& Suppliers
Can Deliver
Product X’s
Needs & Wants, Functions
Controlling the Critical Requirements

## Slide 109: Variation Prediction “Schematic”
CTQ
Target
LSL
USL
Sigma
Target
Mean
Std.
Dev.
DPU
Predicted
Sigma
GAP Analysis and Iteration
Define Design & Lower Level Requirements
Design
Capability Prediction
USL
Requirements
Design Prediction
VOC – CTQs
Design Process
Define Requirements
Develop Design
Develop More Details
Assess Capability
Not OK
(To Production)
OK
V&V
Design Scorecard!

## Slide 110: Scorecard Structure
A “Typical” Design Scorecard
CTQs Listed
Capability Prediction: OK!
Capability Prediction: Not OK!
Measure Needed

## Slide 111: CTQ Scorecard “Maturity” - Prediction
Measure
Explore
Design
Define CTQ’s
Optimize to CTQ’s

## Slide 112: CTQ Scorecard “Maturity” - Verification
Validate Process’ Ability to Deliver CTQ’s
During Design Verification
During Process Validation
Verify/Validate
Verify CTQ’s

## Slide 113: Prediction Exercise
Objective | Develop Quality Predictions
Instructions | Complete the Design Scorecard calculations on the following page. How well is this design predicted to perform?
Time | 10 minutes

## Slide 114: Design Scorecard Exercise
CTQ | Metric | Lower | Target | Upper | Cpk Target | Mean | Std. Dev. | Cpk Pred.
Force | Newtons | NA | NA | 100 | 1.33 | 90 | 4 | 
Speed | Cm/Sec | 15 | 25 | NA | 1.00 | 24 | 3 | 
Articulation | Degrees | 25 | 30 | NA | 1.5 | 30 | 1.5 | 
. . . . . . |  |  |  |  |  |  |  | 
Complete This Column

## Slide 115
erify Versus
Design Validation
Product = Customer Needs + Intended Uses
Is it what customer wants?
DESIGN VERIFICATION
DESIGN VALIDATION
Product
Release
Design Input
Customer + Performance Rqmts.
Customer Req’t Performance Req’t;
or Performance System or Sub-System
Requirement Requirement
Design Output
Acceptance Criteria
Design Verification
Output = Input
Do we meet our specs?
alidate
erify
alidate
V&V Illustrated
Verification & Validation

## Slide 116: QFD References
Quality Function Deployment, Lou Cohen
Better Designs in Half the Time, Bob King

## Slide 117: Revision Control
Date | Changes
Aug 2026 | Rev. 0 - Baseline